## Slide 1: Recent enhancements of the OTIS model to simulate multi-species reactive transport in stream-aquifer systems.
Ryan T. Bailey
Department of Civil &
Environmental Engineering

## Slide 2: OTIS
Overview of Presentation
Arkansas River Basin, CO
Fate and transport of Nitrogen, Selenium species (remediation) in river network.
Modifications to OTIS code
Fertilizer
Shale

## Slide 3: Background & Motivation
Need tool to simulate in-stream solute concentration in groundwater-driven watersheds
Assess influence of remediation strategies (BMPs) on in-stream concentration of NO3 and Se species
Groundwater solute concentration (NO3, Se)
Solute mass loadings to Arkansas River
Irrigated
Fields
What about in-stream solute concentration?
Groundwater flow model
(MODFLOW-UZF1)
Reactive transport model
(UZF-RT3D)
Selenium
Nitrate
All river segments impaired for Selenium
(4.6 µg L-1 for Aquatic Life)

## Slide 4: Project Objectives
Identify effective regional-scale remediation strategies to decrease in-stream concentrations of Selenium and Nitrate
I. Develop model for Se and N transport in Streams (OTIS)
1. Network of Connected Streams
2. Interaction between Chemical Species
3. Nitrogen Cycling Processes
4. Selenium Cycling and Transformation
5. Apply model to Arkansas River Basin (Testing, Sensitivity Analysis)
II. Couple model with UZF-RT3D (groundwater-surface water)
III. Explore remediation strategies

## Slide 5
Model Requirements
- Handle Steady and Unsteady Flow
- Inputs/Outputs (mass loading from aquifer)
- Multiple solutes
Model Development
- Base Model: OTIS (One-Dimensional Transport with Inflow & Storage) (Runkel, 1998)
Apply to Stream Networks
Chemical reactions / transformations (interacting species)
Nitrogen cycling, Selenium cycling and transformation
I. Develop model for Se and N transport in Streams
Modifications

## Slide 6
- Handle Steady and Unsteady Flow
- Inputs/Outputs (mass loading from aquifer)
- Multiple solutes
Apply to Stream Networks
Chemical reactions / transformations (interacting species)
Nitrogen cycling, Selenium cycling and transformation
I. Develop model for Se and N transport in Streams
Stream Network
Mass balance
Input Files: Parameters for each stream
Model Requirements
Notes: Loop through streams in the code.
Mass at the junctions.
Files modified to include parameters for each stream.

## Slide 7
- Handle Steady and Unsteady Flow
- Inputs/Outputs (mass loading from aquifer)
- Multiple solutes
Apply to Stream Networks
Chemical reactions / transformations (interacting species)
Nitrogen cycling, Selenium cycling and transformation
I. Develop model for Se and N transport in Streams
Model Requirements
Concentration of Solute 1  Affects concentration of Solute 2
 System of differential equations
 Solve using 4th-order Runge-Kutta method
Notes: Loop through streams in the code.
Mass at the junctions.
Files modified to include parameters for each stream.

## Slide 8
- Handle Steady and Unsteady Flow
- Inputs/Outputs (mass loading from aquifer)
- Multiple solutes
Apply to Stream Networks
Chemical reactions / transformations (interacting species)
Nitrogen cycling, Selenium cycling and transformation
I. Develop model for Se and N transport in Streams
Model Requirements
Algae
Oxygen O2
Photosynthesis
Algal Respiration
Atmospheric
Reaeration
Nitrification of
NH4, NO2
Decompose organics
Sediment demand
Organic N
NH4
NO2
NO3
Groundwater
Groundwater
Uptake
Uptake
Biomass to N
Settling
Diffusion from
Sediments
Denitrification
Min.
Nitrif.
Nitrif.
QUAL2E
OTIS Input File
Notes: Loop through streams in the code.
Mass at the junctions.
Files modified to include parameters for each stream.

## Slide 9
- Handle Steady and Unsteady Flow
- Inputs/Outputs (mass loading from aquifer)
- Multiple solutes
Apply to Stream Networks
Chemical reactions / transformations (interacting species)
Nitrogen cycling, Selenium cycling and transformation
I. Develop model for Se and N transport in Streams
Model Requirements
Algae/
Aquatic Plants
Org Se
SeO4
SeO3
Se2-
Se
Volatil.
SeMet
Groundwater
Respiration
Settling
Min.
Volatiliz.
Uptake
Uptake
Sorption
Red.
Red.
Red.
+
Notes: Loop through streams in the code.
Mass at the junctions.
Files modified to include parameters for each stream.

## Slide 10
I. Develop model for Se and N transport in Streams
Sensitivity Analysis
Apply model to Arkansas River Basin
Assess influence of parameters on NO3 and O2
OTIS grid
34 flow and transport parameters
Steady flow in Arkansas River
6 Tributaries
2006-2008 simulation period
Processing SA Results:
Sensitivity indices
Temporal values of indices
Spatial values of indices

## Slide 11
I. Develop model for Se and N transport in Streams
Transient Flows
Apply model to Arkansas River Basin
Flow rates: MODFLOW-SFR
Transient upstream BC for O2, NO3, and SeO4
Field work: sample Se in water, sediments, stream bank
Compare against in-stream O2, NO3, and SeO4
2006-2010
(12 sampling events)
Sampling sites

## Slide 12
Groundwater
Solute Transport
REACTIVE
TRANSPORT
UZF-RT3D
Surface Water
Solute Transport
OTIS*
Solute
mass depletion
Solute
mass loading
Discharge
Seepage
CD
CS
CD
CS
Groundwater
Flow
Surface Water
Flow
FLOW
Stream
Seepage
MODFLOW-UZF
SFR2 Package
Groundwater
discharge
Linker file
Output (Q, depth, lateral inflow,…)
II. Couple Model with UZF-RT3D
Imbedded within RT3D
Groundwater-Surface Water Coupling

## Slide 13
Groundwater flow model
(MODFLOW-UZF1)
Reactive transport model
(UZF-RT3D)
(Eric Morway, USGS)
(N, Se cycling packages)
Stream Network
Flow Model: SFR2 package for River, Tributaries
Sampling
Sites
Divided into stream segments
Transport Model: QUAL2E parameter values
Testing Data: Stream flow, stream depth
In-stream conc. of O2, NO3, SeO4
II. Couple Model with UZF-RT3D
Groundwater-Surface Water Coupling

## Slide 14
Rocky Ford
gage
La Junta
gage
Preliminary RT3D-OTIS simulations
II. Couple Model with UZF-RT3D
Groundwater-Surface Water Coupling

## Slide 15: Next Phases
Further Calibration/Testing of RT3D-OTIS model
Explore Effect of Remediation Strategies
Reduce irrigation
Reduce canal seepage
Reduce Nitrogen fertilizer loading
Implement/Enhance Riparian buffer zones