## Slide 1: Fracture Transmissivities Before And After Hydrofracturing Water Wells In Granitic Bedrock
David Hart

## Slide 2: Location
Notes: Looked to the Granites in Marathon County first.

## Slide 3: Motivation
Low yields from crystalline bedrock.
Glacial material thin.
Wells hydrofractured to increase yield
Hydrofracturing done in this region since the 1970s
National Driller (2005) - Haupt
Notes: Looked to the Granites in Marathon County first.

## Slide 4: Geothermal 1
Many fractures over entire depth
Gamma spikes correlate (uranium)
Orthogonal fracture sets

## Slide 5: Geothermal 3
Fewer fractures over entire depth
Gamma spikes correlate (uranium)
Homogeneous lithology

## Slide 6: Hydrofracturing Record
Lithostatic Stress (psi)
10 MPa
5 MPa
Geothermal 1

## Slide 7
Lithostatic Stress (psi)
10 MPa
5 MPa
Geothermal 3

## Slide 8
Lithostatic Stress (psi)
10 MPa
5 MPa
Geothermal 3

## Slide 9
Lithostatic Stress (psi)
10 MPa
5 MPa
Geothermal 3

## Slide 10
Lithostatic Stress (psi)
10 MPa
5 MPa
Geothermal 3

## Slide 11: Hydrofracture Reports
Geothermal 1
  More Fractures ( 423 identified)
  Lower cracking pressures < 1700 psi (11 MPa)
  Unlikely any new fractures formed
Geothermal 3
  Fewer Fractures (90 identified)
  Higher cracking pressures 3000 psi (21 MPa)
  Possibly creating new fractures.
Lab tensile strengths (Goodman, 1989)
  Nevada Test Site granite 1700 psi (11.7 MPa)
  Pikes Peak granite 1730 psi (11.9 MPa)

## Slide 12: Measuring Transmissivities
Flow Logging - Weighted Transmissivities
  assumes: steady state, horizontal flow during pumping, and no ambient flow
  Transmissivity of an interval is proportional to the flow from that interval.
Heat Pulse Flow Meter
For more background on flow logging:
http://water.usgs.gov/ogw/bgas/flowmeter/

## Slide 13: Geothermal 1
 | Pre-Hydrofracture | Post-Hydrofracture
Ttotal (ft2/day) | 2.65 | 23.0
8 x overall increase post-hydrofracture

## Slide 14
Two fractures at 201 ft
Create provide most of the yield in this well.

## Slide 15: Measuring Transmissivities
Packer Testing
  Isolate depth interval of interest (2 feet in this study)
  Conduct Slug test

## Slide 16: Geothermal 3
 | Pre-Hydrofracture | Post-Hydrofracture
Ttotal (ft2/day) | 0.54 | 34
65 x overall increase post fracture

## Slide 17
These two fracture are more transmissive than most in this well

## Slide 18: Conclusions
Hydrofracturing increased well yields by 1 to 2 orders of magnitude.
Fractures present from surface to 1000 feet.
  Lots of fractures (Geothermal 1) – no new fractures generated during hydrofracture process
  Few fractures (Geothermal 3) – some new fractures generated but not important for well yield.
Variation or shape of transmissivities with depth remained relatively constant
  All the transmissivities shifted or increased.
  Low T zones moved higher but remained low T zones relative the high T zones.
Recommendation - Spend time and effort on high T zones in upper part of the well

## Slide 19: Geology of Boring Locations
Geothermal 3 – Granite & Quartz Monzonite
Geothermal 1 - Granite