## Slide 1: CASE STUDIES OF CHROMITE ORE PROSPECTING IN CAMAGUEY PROVINCE, CUBA
Rubén González Pontón
Sociedad Cubana de Geología
2016 Geological Society of America Annual Meeting
Denver, Colorado. United States of America
24 – 28 September 2016

## Slide 2: DISTRIBUTION OF OPHIOLITES IN THE ISLE OF CUBA
0 100 200 km
SEPTENTRIONAL OPHIOLITES
AMPHIBOLITIZED OPHIOLITES
Iguará-Perea
Cajálbana
La Habana
Matanzas
Section of ophiolites in Camagüey
Moa -Baracoa
Santiago de Cuba
Holguín
Mayarí
Camagüey
Mabujina
Yayabo
Jagua
Santa Clara
Isla de la Juventud
Sierra del Convento
Güira de
Jauco
THERE ARE LOTS OF OPHIOLITES IN CUBA AND MANY OF THE ULTRAMAFIC SECTIONS HOST IMPORTANT CHROMITE BODIES. THE ABUNDANCE OF CHROMITE ORE DEPOSITS IN CAMAGÜEY HAS ATTRACTED THE ATTENTION OF PROSPECTORS SINCE THE EARLY 20th CENTURY AND HELPED CUBA REACH PROMINENCE IN THE EXPORT OF CHROMITE DURING THE SECOND WORLD WAR.

## Slide 3: LOCATION OF CHROMITE ORE DEPOSITS AND SHOWINGS
MEDIUM TO LARGE DEPOSITS OF REFRACTORY CHROMITE WERE DISCOVERED DURING THAT EPOCH. MAJOR MINES WERE RAFAEL, AVENTURA, LOLITA, VICTORIA WITH MORE THAN 200 000 t EACH.
HUNDREDS OF CHROMITE ORE DEPOSITS AND SHOWINGS ARE LOCATED AT DIFFERENT LEVELS OF THE OPHIOLITIC SECTION.

## Slide 4: LOCATION OF CHROMITE ORE DEPOSITS AND SHOWINGS
FOR THE FIRST TIME ADAIR E. L. PERFORMED IN 1937 A GEOPHISYC SURVEY USING THE TORSION BALANCE.
PROSPECTING WORKS WERE CARRIED OUT BY THAYER T. P. EN 1942; DELOS E. FLINT, JESÚS FRANCISCO DE ALBEAR Y PHILIP W. GUILD IN 1948, ALSO GRAVITY SURVEYS IN 1942 - 1943 AND 1954 - 1956 BY U. S. GEOLOGICAL SURVEY. THE BIGGEST DEPOSIT CAMAGUEY – II WAS DISCOVERED AT THAT TIME (700 800 t)
PROSPECTING FOR CHROMITE IN OPHIOLITIC BODIES RENEWED AFTER 1962 IN COLLABORATION WITH RESEARCHERS FROM EASTERN EUROPE.
AVENTURA MINE

## Slide 5: LOCATION OF CHROMITE ORE DEPOSITS AND SHOWINGS
A CUBAN-GERMAN CREW OF GEOLOGISTS AND GEOPHYSICISTS PERFORMED TWO PROJECTS IN 60 Km2 FOR CHROMITE PROSPECTING FROM 1983 – 1987 AND FROM 1987 – 1990 IN THESE SECTORS.
THE LOCATION OF THE TWO SITES TREATED AS CASE STUDIES IS HIGHLIGHTED HERE.

## Slide 6: METHODOLOGY
SELECTION OF SECTORS
TOPOGRAPHIC SURVEY - DIGITAL MODELING OF THE TERRAIN
GRAVITY SURVEY
MAGNETIC SURVEY
GEO-ELECTRICAL SURVEY
CONSTRUCTION OF 50 x 20 m GRID
GEOLOGIC MAPPING
BOUGUER MAP
CALCULATION OF LOCAL GRAVITY FIELD
GEOLOGIC MAP
MAGNETIC MAP
GEO-ELECTRICAL DATA
TOPOGRAPHIC CORRECTION
GEOLOGIC CRITERIA
GEOPHYSICAL CRITERIA
CATALOG OF ANOMALIES
SELECTION OF DRILLING TARGETS
BASED ON THE DENSITY CONTRAST BETWEEN CHROMITITES AND HOST SERPENTINIZED PERIDOTITES, GRAVITY SURVEYS WERE THE PRIMARY EXPLORATION METHOD. VALUES OF DENSITY FOR ENCLOSING ROCKS VARY FROM 2.4 TO 2.5 g/cm3 WHILE THE ESTIMATED DENSITY FOR THE CHROMITE ORE AVERAGES 3.7 g/cm3.

## Slide 7: METHODOLOGY
REQUIREMENTS FOR GRANTING ANOMALY CLASS
GRAVITY ANOMALY | POLARIZABILITY ηa | RESISTIVITY ρa | MAGN. FIELD ∆ T | CLASS (K) OF ANOMALY
+ | MINIMUM | MAXIMUM | MINIMUM | 1
+ | - | - | WEAK GRADIENT | 2
± | - | - | - | 3
- | - | - | - | 4
GRAVITY ANOMALY | CLASS OF ANOMALY (K) | QUANTITY OF GEOLOGICAL CRITERIA | PROSPECTIVENESS P
+ | 1,2 | 2 | 1
+ | 1,2,3 | AT LEAST 1 | 2
+ ± | 1,2,3 | 1 PARTIALLY | 3
- | 1,2,3,4 | - | 4
IF A POSITIVE LOCAL GRAVITY ANOMALY IS CHARACTERIZED WITH MINIMUM OF POLARIZABILITY, MAXIMUM OF RESISTIVITY AND MINIMUM OF MAGNETIC FIELD, THE ANOMALY BELONGS TO THE FIRST CLASS.
REQUIREMENTS FOR GRANTING ANOMALY PROSPECTIVENESS
FIRST AND SECOND CLASSES OF ANOMALIES THAT MATCH AT LEAST TWO GEOLOGICAL CRITERIA BELONG TO THE P1 PROSPECTIVENESS

## Slide 8: METHODOLOGY
mgl
0.10
0.15
0.20
0.05
0
- 50 -25 0 25 50 m
1
2
H = 10 m
-50 -25 0 25 50 m
H = 20 m
-75 -50 -25 0 25 50 75m
H = 30 m
-75 -50 -25 0 25 50 75m
H = 50 m
ORE BODY 1
30 m
10 m
50 m
ORE BODY 2
30 m
5 m
100 m
ANOMALY´S INTENSITY DEPENDENCE OF DISTURBER BODY´S DIMENSIONS
52 500 t for chromite density σ = 3 500 Kg . m-³
- 10 -5 0 5 10 m
90°
- 10 -5 0 5 10 m
60°
0.10
0.08
0.06
0.04
0.02
mgl
- 10 -5 0 5 10 m
45°
- 10 -5 0 5 10 m
60°
Angle of dipping
At 5 m
depth
At 10 m
depth
20 m
30 m
5 m
ANOMALY´S INTENSITY DEPENDENCE OF DISTURBER BODY´S DEPTH AND DIPPING
10 500 t for chromite density σ = 3 500 Kg . m-³
MODELING OF CHROMITE BODIES TOOK IN ACCOUNT THE DIMENSIONS, DEPTH AND DIPPING OF DISTURBER OBJECTS.

## Slide 9: CASE STUDY No. 1. VICTORIA - I
Victoria - I sector . A = 4.8 Ha
BELONGS TO THE CUMULATIVE COMPLEX OF OPHILITE ASSAMBLAGE
SERPENTINIZED HARZBURGITES ARE THE PREDOMINANT ROCK TYPE
(Up to 2.70 g/cm3 DENSITY)
SUBORDINATED SERPENTINIZED DUNITES
GABBROID BODIES OF MODERATE DIMENSIONS AND OLIVINIC COMPOSITION
GABBRO DIKES (Average density 2.85 g/cm3)
THE SECTOR IS BY THE SIDE OF EXHAUSTED CHROMITE MINE

## Slide 10: INTERPRETATION OF GEOPHYSICAL AND GEOLOGICAL DATA
M
s
s
M
M
?
?
ᴦ
M
ᴦ
ᴦ ᴦ
M
M
?
2
22
SECTIONS
4
6
8
10
12
14
16
18
20
220 m
200 m
180 m
160 m
140 m
120 m
100 m
80 m
60 m
40 m
20 m
0 m
M
G
G
M
M
?
M
G
vvv
M
M
G
M
M
M
G
G
G
G
G
G
M
M
M
M
M
M
M
M
M
M
vvv
vvv
s
s
s
s
s
s
s
s
s
s
s
s
s
s
s
ᴦ
ᴦ
ᴦ
ᴦ
ᴦ
ᴦ
M
M
M
G
G
G
vvv
M
M
M
M
M
M
M
s
s
s
M
BY MAGNETIC SURVEY
vvv
BY INDUCTIVE POLARIZATION
WITH DIRECTION OF DIPPING
G
BY GRAVITY SURVEY
INTERPRETED FAULTS
CHROMITE ORE BODIES
PROJECTION TO THE SURFACE
ACCORDING RESULTS OF DRILLING
MINIMUM OF MAGNETIC FIELD LINE 300 ηT
LOCAL GRAVITY ANOMALY
LINE 0.6 * 10-6 m.s-2 GRIFFIN r = √‾s s = 20
HOLES POSITIVE
NEGATIVE
HOLES VERTICAL
AT ANGLE
SERPENTINIZED PERIDOTITES
LITHOLOGY
NON DIFFERENTIATED GABBROS
GRAVITY AND MAGNETIC SURVEYS AND I. P. HELPED MAPPING OF DISTURBED SURFACE BY HUMAN ACTIVITIES, ALSO THE INTERPRETATION OF TECTONIC STRUCTURES.
INTERPRETATION WAS UPDATED LATER WITH THE OUTCOMES OF EXPLORATION DRILLING.
IN RED COLOUR THE DRILL HOLES THAT INTERCEPTED THE ORE BODIES, THE BLUE ONES DID NOT.

## Slide 11: INTERPRETATION OF GEOPHYSICAL AND GEOLOGICAL DATA
DISCONTINUOS LINES ARE THE CONTOURS OF THE ORE BODIES ± MATCH THE LINE (IN BLUE COLOUR) OF VALUES 0.6 * 10-6 m.s-2 EXCEPT ONE HOLE IN SECTION 14.
FOR ESTIMATION OF RESOURCES WE USED THE INTERPOLATION TO HALF OF THE DISTANCE BETWEEN TWO HOLES BUT NATURE DOESN´T UNDERTAND RULES….
60
80
100
120
140
65.00
90.00
90.00
ORE BODY No. 1
ORE BODY No. 2
50.00
ᴦ
ᴦ
ᴦ
S
S S
S
S S
S
S S
S
S
S
S
S S
S
S S
S
SECTION 14

## Slide 12: INTERPRETATION OF GEOPHYSICAL AND GEOLOGICAL DATA
INTERPRETATION FROM LOCAL GRAVITY MAP MADE POSSIBLE TO IDENTIFY TWO ANOMALIES SHOWING ORE BODY, PROBABLY BROKEN IN TWO PARTS AS RESULT OF EMPLACEMENT OF OPHILITES AND TECTONIC STRUCTURES. THAT IDEA IS SUPPORTED BY EXPLORATION DRILLING IN THE NEXT SLIDE.

## Slide 13: INTERPRETATION OF GEOPHYSICAL AND GEOLOGICAL DATA
SECTION 10
ᴦ
ORE BODY No. 1
ᴦ
48.40
70 m
60 m
50 m
40 m
30 m
20 m
10 m
0 m
ᴦ
40
60
80
100
120
140
ᴦ ᴦ
87.40
100.90
ᴦ ᴦ
ᴦ ᴦ
S
S S
S
S
S S
S
S
S S
S S
S
S
S S
S
SECTION 12
70 m
60 m
50 m
40 m
30 m
20 m
10 m
0 m
65.50
113.60
100.00
80.00
34.90
ORE BODY No. 1
ᴦ
ᴦ
ᴦ
ᴦ
ᴦ
ORE BODY No. 2
40
60
80
100
120
140
S
S S
S
S
S S
S
S
S S
S
S S
S
S
S S
S
S
S S
S
S S
TWO ORE BODIES DIPPING SW TO THE CONTACT OF SERPENTINITES WITH THE GABBROID BODY

## Slide 14: INTERPRETATION OF GEOPHYSICAL AND GEOLOGICAL DATA
MAGNETIC FIELD REVEALED TWO MINIMUMS IN THE AREA OF GRAVITY ANOMALY (DISCONTINUOS GREEN LINES).

## Slide 15: COMPLEX INTERPRETATION FOR SECTION 10 IN VICTORIA - I
FROM I. P. – TRIELECTRODIC PROBE: NO CONCLUSIVE INDICATIONS ABOUT THE EXISTENCE OF ANY ORE BODY, JUST TWO SITES OF MODERATE RESISTIVITY. ONLY VALID INFORMATION IS THE POSSIBLE EXISTENCE OF FAULTS, DIPPING SW TO THE CONTACT WITH GABBROS.
MEDIUM GRADIENT MAPS OF POLARIZABILITY AND RESISTIVITY DO NOT SHOW ANY POSSIBLE TECTONIC ELEMENT.
2.5
2.6
2.6
2.8
2.1
2.3
2.3
2.5
2.6
2.4
2.6
2.5
3.8
ᴦ
ᴦ
ᴦ
ᴦ
3.6

## Slide 16: CASE STUDY No. 1. VICTORIA - I
THE GRAVITY SURVEY REVEALED THE ANOMALY VICTORIA-I AND LATER EXPLORATION BECAME THE DEPOSIT INTO THE FIRST OPEN CAST MINE RESULTED FROM THIS RESEARCH.
MASSIVE ORE AND MINOR DENSE DISSEMINATED CHROMITE WITH AVERAGE CONTENTS:
Cr2O3: 29.20 % SiO2: 6.5 % Al2O3: 26.90 CaO: 0.9 %

## Slide 17: CASE STUDY No. 2. MINAS SUR
Minas Sur Area: 2.50 Km2
BELONGS TO THE CUMULATIVE COMPLEX OF OPHILITE ASSAMBLAGE
HIGH DENSITY SERPENTINIZED HARZBURGITES ARE PREDOMINANT
(Up to 2.85 g/cm3 DENSITY)
THERE ARE LESS SERPENTINIZED DUNITES
GABBROID BODIES OF MODERATE DIMENSIONS AND OLIVINIC COMPOSITION
GABBRO DIKES (Average density 2.85 g/cm3)
BASALTS AND DIABASES (Up to 2.99 g/cm3)
MANY SURFACE FRAGMENTS OF MASSIVE CHROMITE-FLOATING CHROMITE

## Slide 18: CASE STUDY No. 2. MINAS SUR
BOGUER GRAVITY MAP
LOCAL GRAVITY MAP
MAGNETIC FIELD MAP
SHOWS MANY GRAVITY ANOMALIES. IT WAS THE BASIS TO SET AREA TO DENSIFY SURVEY USING 25 x 10 m. GRID
REVEALED CLEAR DEFINITION OF
GRAVITY ANOMALIES 0.02 TO 0.08 mlg.
SUPPORTED THE SELECTION OF THE DENSIFICATION AREA WITH A FIELD OF MINIMUM VALUES.

## Slide 19: CASE STUDY No. 2. MINAS SUR
600
500
400
300
20
22
24
26
28
30
32
34
36
38
40
600
500
400
300
20
22
24
26
28
30
32
34
36
38
40
0.1
0
0
0
0
0.02
0.02
0.02
0.02
-0.02
-0.04
0.02
0.04
0.08
0.06
0.06
0.06
0.06
0.06
0.06
0.06
0.04
0.06
0
-0.04
Vertical testing
drill holes
Inclined testing
drill holes
GEOLOGIC MAP OF SELECTED AREA. GRID 25 X 10 m
LOCAL GRAVITY MAP AND DRILLING TARGETS
Serpentinized peridotites
Serpentinized
dunites
Observed
faults
Possible
faults
Gabbro dikes
Floating
chromite
GEOLOGIC MAPPING REVEALED FAVORABLE CRITERIA: A WIDE SITE OF FLOATING CHROMITE, SOME DUNITE LENSES IN THE BACKGROUND OF SERPENTINIZED PERIDOTITIES AND DIKE SWARMS.
ONCE BEING PREPARED THE ANOMALY´S CLASSIFICATION CATALOG, CAME OUT DRILLING TARGETS TO BE CHECKEP UP.

## Slide 20: CASE STUDY No. 2
ACCORDING THE RESULTS OF MAPPING, TRENCHES AND DRILLING, THE CAUSES OF THE 69 GRAVITY ANOMALIES ARE:
DRILLING SHOWED THAT THE NATURE OF DISTURBER BODY FOR THE 16 CHECKED UP ANOMALIES WAS:
THE UNEXPECTED RESULT IS THAT NO BLIND CHROMITE ORE BODY FOUND IN MINAS SUR AREA.
VERY DENSE HARZBURGITES | 50
DIABASES AND BASALTS | 12
GABBRO DIKES | 7
VERY DENSE HARBURGITES | 10
DIABASES AND BASALTS | 3
GABBRO DIKES | 3

## Slide 21: CASE STUDY No. 2. MINAS SUR
SECTION OF DRILL HOLES OVER THE MOST PROSPECTIVE AREA
2.56
S
S
S
S
S
S
S
S
ᴦ
0 m
10 m
20 m
30 m
40 m
50 m
60 m
70 m
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
ᴦ ᴦ ᴦ
ᴦ ᴦ
ᴦ
ᴦ
D D D
D D
D D D
2.5
2.84
2.46
2.56
2.83
2.69
2.57
2.58
2.77
2.60
2.59
2.84
2.59
S
S
S
60.00
60.00
96.60
11-BD5
2-BD5
1-BD5
S S
D D
2.84
SERPENTINIZED PERIDOTITIES
SERPENTINIZED DUNITES
GABBRO
MEASURED DENSITY
USING MEASURED DENSITY, THE DETAILED STUDY OF ANOMALIES DEMONSTRATED THAT THE CAUSES WERE GABBRO DIKES AND VERY DENSE PERIDOTITES.

## Slide 22: CONCLUSIONS
GRAVITY SURVEY IS THE MOST EFFECTIVE METHOD FOR PROSPECTING OF BLIND CHROMITE ORE BODIES.
MAGNETIC SURVEY PLAYS A SIGNIFICANT ROLE FOR DETERMINING TECTONIC STRUCTURES.
THE OUTCOMES OF ELECTRICAL METHODS ARE AMBIGUOUS IN MANY CASES.
MAJORITY OF ANOMALIES HAS THE CAUSE IN DENSE HARZBURGITES BLOCKS, MANY ARE PROVOKED BY GABBROS, LESS BY VOLCANIC ROCKS.
THERE ARE MANY GEOLOGICAL CRITERIA THAT PLAY AN OUTSTANDING ROLE IN PROSPECTING OF CHROMITE.
DETAILED PROSPECTING HAS COVERED RELATIVELY SMALL AREAS IN OPHIOLITES, SO THE PROSPECTIVENESS IS WIDE FOR DISCOVERING NEW BLIND CHROMITE BODIES.

## Slide 23
Thanks