## Slide 1
Utilizing image recognition technology for foraminiferal assemblage analyses
Christian H Gfatter

## Slide 2: Florida Springs Coast

## Slide 3: Traditional picking
Pick
Arrange
Store

## Slide 4: Identification
Novice
Expert
familiar with > 100 genera or species
Identified | using pictures | using electronic dichotomous key | using available resources
Genera | 57 of 60 | 56 of 60 | 60 of 60
species | 7 of 57 | 14 of 56 | 30 of 60
time | 2 hours | 3 hours | 1.5 hours
estimated correct | TBD | TBD | > 95%
Requires skill developed over years
Notes: Broken & tiny forams might not be identifiable or only identifiable to a certain level
Still subjective, like balls & strikes being called by a minor league umpire vs. a major league umpire. i.e., Called to the best of their ability, but that strike could have been a ball.

## Slide 5: The Big Idea
Software generates data which allows writing detailed Thesis
Add sediment containing foraminifera
Machine sorts & processes particles
Software generates Thesis

## Slide 6: Imaging Instruments
FlowCam® VS Series (2 µm to 2 mm particles)
Output from sediment sample
Images selected as forams

## Slide 7: Imaging Instruments
ZooSCAN (liquid zooplankton)
Images of 11 forams
using the lower light

## Slide 8: Imaging Instruments
ZooSCAN (liquid zooplankton)
Images of 11 forams
using the upper light

## Slide 9: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Archaias angulatus

## Slide 10: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
20 x
focused on largest foram

## Slide 11: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
25 x
focused on largest foram

## Slide 12: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
32 x
focused on mid-sized foram

## Slide 13: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
40 x
focused on mid-sized foram

## Slide 14: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
40 x
focused on smallest foram

## Slide 15: Imaging Instruments
Zeiss AxioCam MRc5 (5 megapixel digital microscope camera)
Magnification
40 x
Archaias angulatus
Additional set of images taken for larger specimens
20 x
Archaias angulatus

## Slide 16: Micropaleoslide arrangement
1 slide per site
1+ forams per grid
1/4 of grid utilized with forams grouped by size
Library images from sites
1+ slides per site
1 foraminifera per grid
Several views photographed
Sampling site images

## Slide 17: Combining AxioCam pictures with FlowCam image processing software
images
VisualSpreadsheet
AVI animation

## Slide 18: Video used by FlowCam software (VisualSpreadsheet) For this demo, 48 images at 6 frames per second

## Slide 19: VisualSpreadsheet output

## Slide 20: Refinement
Initial classification and measurements systematically made by software
Manual post-processing: image rejection, identification overrides, etc.
Library grows, helping improve processing of subsequent foraminiferal samples
Digital data (images & records) can be shared and backed-up (physical specimens archived)
Notes: Automatic IDs may not be exact, but it should aid manual work
Software gets better and better

## Slide 21: Potential Applications & Considerations
SOFTWARE: other programs (e.g. SIPPER) may make finer determinations, provide different data, etc.
WHAT: heavy mineral sands (e.g., in ancient beach sands), diatoms, ostracods, & other opaque organisms
HOW: using trichloroethylene (TCE) separation technique to provide foraminiferal samples for bulk processing
Notes: • TCE might speed up the number of images taken, or be utilized to create aliquots of forams to be processed by machine (automated, but currently black & white images)
• There is better (as well as other) software & technology available, but these were within our area and budget to explore

## Slide 22: Summary
Broeckina orbitolitoides
Additional data
    Standardized characterization (e.g. length)
Identification efficiency
    Consistency
    Error reduction
Digitization
    Accessibility
    Global sharing

## Slide 23: Acknowledgements & Credits
Maps:
Florida Center for Instructional Technology, University of South Florida
Images:
www.fluidimaging.com/products/flowcam-vs
www.hydroptic.com/zooscan.html
commons.wikimedia.org
cliparts.co
Cushman Foundation for Foraminiferal Research
Dr. Pamela Hallock Muller
Kyle Amergian
Harry Nelson, VP – Aquatic Markets, Fluid Imaging Technologies
Ian W Bishop, University of Colorado
Kate Dubickas
Dr Paul Carlson, Florida Fish and Wildlife Research Institute

## Slide 24: Questions

## Slide 25: Thank you!
Christian H Gfatter
+1 (312) 321-1777 cgfatter@mail.usf.edu