## Slide 1
Sediment thickness
SEDIMENT STORAGE TIME IN A SIMULATED MEANDERING RIVER’S FLOODPLAIN: COMPARISONS OF POINT BAR AND OVERBANK DEPOSITS
Tobias Ackerman | Jim Pizzuto | University of Delaware | GSA | 2016
tobiack@udel.edu
NSF EPSCoR 11A-1301765

## Slide 2: Why Sediment?
May 6, 2013
~ Its how the mountains travel to the sea
Geology
  Earth history is recorded in sedimentary rocks
Environment
  Sediment plays an outsized role in aquatic environments

## Slide 3: Why Floodplain Storage?
~ Its about time
Geology
  Source to sink signal lag
Environment
  Direct sediment & pollutant supply to waterway
  Re-emission of trapped ‘contaminants’

## Slide 4: Modeling effort
Simulate a meandering river
Deposit ‘sediment’ in 2 facies
  Point bar deposits
  Overbank (vertical accretion) deposits
Caveats
  No channel incision or aggradation
  No valley walls, or processes shorter than 30 years
  Uniform erodibility, and hydrograph
Track the age of sediment when its eroded
Research findings
Overbank storage has a heavier distirbution than point bar storage.
Distributions become light tailed
Less valley confinement leads to heavier tails

## Slide 5
10 km
Channel centerline simulation (4ky)
Schwenk et.al. 2015 (Ikeda et.al. 1981)
Flow Q = 325 cms
Flow Depth = 3 m
Valley Slope = 6.7 x 10-4
Channel width = W = 70 m
Dt = 0.17 years
Erodibility (Eo) = 3.7 x 10-8
Floodplain dimensions ±25 by ±33 km
Node spacing 0.28 to 1.9 W (20 to 133m)
Annual migration rate ≈ 5% channel width
Migration = f(Substrate erodibility, curvature, flow)

## Slide 6: Planform Scale
10 km
Meander wavelength
Sinuosity (tortuosity)
Way too high:
Leopold & Wolman 1957,
Schumm 1963
27 w
4

## Slide 7: Planform Scale
10 km
Meander wavelength
Sinuosity (tortuosity)
Way too high:
Leopold & Wolman 1957,
Schumm 1963
Adjust
Friction factor
Cross slope factor
Erodibility constant
Violates hydrodynamics
10 km
27 w
4
12 w
3.2

## Slide 8
Floodplain deposition rates
  probably decrease with elevation
  and distance from channel
Point bar deposition is abrupt
Dh = Change in elevation
h = Elevation max & actual
D = Distance to channel
Dh = (hmax – hact) [n + m e(-D/l)]
(after Howard, 1992)
n = ‘Pelagic’ fine sedimentation rate
m = ‘Diffusive’ coarse sedimentation rate
l = Diffusive length scale
Stratigraphic Column

## Slide 9
Floodplain elevation simulation 6–9 ky
Sediment thickness
10 km
Cool colors are older and higher elevation
Channel margin is mostly warmer colors
Channel width = W = 70 m | Pixel size = W/5 = 14 m | Dt = 30 years

## Slide 10
Flow

## Slide 11
Migration direction
channel
channel
Thick blocks of basal point bar deposits
Thin layers of younger overbank deposits
Scroll bars? (arrows)
Floodplain becomes smoother with time
Younger deposits
Stratigraphic cross-section of sediment age

## Slide 12
channel
channel
Stratigraphic cross-section of sediment age
Dh = (hmax – hact) [n + m e(-D/l)]
(after Howard, 1992)
Overbank deposition rate
  with elevation
  with distance from channel
H = max floodplain height | m = 0.0025*H | n = 0.008*H | l = 0.5*W

## Slide 13
(ky)
Storage time results

## Slide 14: Channel frequents center of floodplain
Upstream
Downstream

## Slide 15
Upstream Point Bar and Overbank storage time distributions
Median

## Slide 16
-0.75
-1
Point bar
peak erosion
Overbank storage has
heavier distribution
Exponential tailing beyond 10 ky indicates equal probability of erosion !
Upstream Point Bar and Overbank storage time distributions

## Slide 17
-0.75
-1
Point Bar and Overbank storage time distributions

## Slide 18: Conclusions
Check planform geometry
Point bars may have a peak contribution
similar to the time to migrate 5-6 W
Overbank storage has a
heavier distribution
Valley confinement influences light tail
Thank you