## Slide 1: Nitrate concentrations in streams as a function of Crop Cover in Midwestern Agricultural Watersheds: Assessing the role of corn and soybeans
Jacob Piske, Eric Peterson, Bill Perry

## Slide 2: Nitrate Problems
Agricultural nonpoint source pollution
  Impairing the water quality in 70% of rivers and streams
Approximately 25% of the NO3- in the stream system will remain mobile and continue to the Mississippi River
Contributes to Gulf of Mexico hypoxia
http://www.feedstuffs.com/news/court-dismisses-setting-pollution-diet-mississippi-river-basin

## Slide 3: Agricultural Influence
Primary source of nutrients to surface water contamination
  Fertilizer use, artificially drained areas, and decreased crop diversity
Average 163 kg ha-1 N-fertilizers applied to corn (USDA, 2016)
Average 20 kg ha-1 N-fertilizers applied to soybeans (USDA, 2015)
http://www.dairymoos.com/shocking-news-the-weather-is-unpredictable/

## Slide 4: N-Fertilizer Rates

## Slide 5: Agricultural Changes
Corn was grown in rotation with alfalfa and clovers
Increased availability of fertilizers and application rate
Intensive subsurface drainage (tile drains)
Current rotation is corn and soybean
Corn was grown in rotation with alfalfa and clovers
Increased availability of fertilizers and application rate
Intensive subsurface drainage (tile drains)
Current rotation is corn and soybean
Corn
Soybeans

## Slide 6: Research Question
Does a relationship exist between nitrate export and crop type (corn or soybean)?
Does nitrate export vary seasonally?

## Slide 7: Watersheds

## Slide 8: Stream Data
Continuous NO3- -N concentrations (mg/L) and discharge (Q, m³) were downloaded from the USGS Water Science Center
Data ranges from 2008 to 2017
Table sorted by percent agriculture
USGS Station | River | Watershed Area (km²) | Percent Agriculture (2017) | NO3 Availability
3336850 | Spoon River | 106 | 92.18% | 2013 – 2017
5554300 | Indian Creek | 175 | 91.65% | 2011 – 2017
5482300 | North Raccoon River | 1813 | 84.26% | 2008 – 2017
5482500 | Raccoon River | 4195 | 84.02% | 2008 – 2017
5447500 | Green River | 2597 | 81.53% | 2015 – 2017
5524500 | Iroquois River | 1162 | 78.49% | 2015 – 2017
5464420 | Cedar River | 16425 | 75.85% | 2012 – 2017
5465500 | Iowa River | 32375 | 70.76% | 2009 – 2017
6481000 | Big Sioux River | 10170 | 59.17% | 2017
6892350 | Kansas River | 154767 | 44.15% | 2013 – 2017
Table sorted by percent agriculture.

## Slide 9: Data Categorization
Year
  April 1 to March 31
Seasons (Hanrahan et al, 2018)
  Spring – April 1 to June 30
  Summer – July 1 to September 30
  Fall – October 1 to December 31
  Winter – January 1 to March 31

## Slide 10: Crop Percentages

## Slide 11: Yearly Corn vs. NO3-Weighted Flow

## Slide 12: Yearly Soybean vs. NO3- Weighted Flow

## Slide 13: Yearly Corn vs. NO3- Load

## Slide 14: Yearly Soybean vs. NO3- Load

## Slide 15: Seasonal Corn vs. NO3- Weighted Flow

## Slide 16: Seasonal Soybean vs. NO3- Weighted Flow

## Slide 17: Relationship – Export vs. Crop Type
Collective Data
  Export increases as corn increases
  Export increases as soybean increases

## Slide 18: Relationship – Export vs. Crop Type
Individual Watersheds
  Export decreases as corn increases
  Export increases as soybean increases

## Slide 19: Conclusions & Future Work
Relationship exist but not as expected.
Season Recap
  Highest export in spring
  Similar export in summer and fall
  Lowest export in winter
Collect crop and stream data for 2018
OR
Collectively
Individual
Hypothesis

## Slide 20: Questions?