## Slide 1: Water Quality Predicting Model in Coal-Mine Impacted Watersheds in Eastern Kentucky
Oguz Sariyildiz, Buddhi Gyawali, George Antonious, Ken Semmens, Demetrio Zourarakis
GSA 2018
Kentucky State University

## Slide 2: Outline
Introduction
Research Problem, Objectives
Methodology
Results & Discussion
Conclusion & Limitations
Acknowledgements & References

## Slide 3: Introduction
Coal is the most important energy resource in Kentucky
Kentucky, the fourth-largest coal mining state, produced more than 39 million tons of bituminous coal in 2016 (EIA, 2017)
87% of Kentucky's net electricity generation was produced by coal (EIA, 2016).
About 162 million tons of coal produced in 1990 (EIA, 2016) at its peak level which is equivalent of 100,000 times volume of Wembley Soccer Stadium.
Tennesee Valley Authority
Caranddriver.com
FIFA.com

## Slide 4: How Coal Mining Affects Environment
Negative influence on local ecologies, stream habitat
Negative impact on hydrology of a watershed
Changes in pH, higher conductivity, and elevated dissolved ions
Valley fills
Forest loss

## Slide 5
Mining percentage is inversely related to local ecology health and water quality,
  However, some of the reclaimed lands turn to reclaimed forest after several years of reclamation.
Influence of reclaimed forests to water quality has not been studied.
Research Problem
Exit Point
Mined (%) | Mined-RF (%) | Rec. Age
40 | 28 | 16 year
Adjusted Mining Percentage
Cumulative Mining Percentage

## Slide 6
Objectives
Identify the correlation between mined areas, reclamation age, and water quality parameters in watersheds mined between 1986-2017;
Investigate the effects of reclaimed forest and reclaimed woods to CMRWQ in watersheds;

## Slide 7: Methodology
NDVI Maps and Vegetation Classification (Barren, Grass, Rec. Woods, Rec. Forest, Unmined)
Water Sampling
Mining Percentage (%)
Vegetation Cover Change (%)
Reclamation Age (years)
Conductivity, Alkalinity, pH, SO4, Mg, Ca, Al, Fe, Mn
Defining Research Area
Correlation Analyses
Mining Percentage (%) – Water Quality Parameters
Vegetation Cover Change (%) – Water Quality Parameters
Reclamation Age (years) – Reclaimed Forest Percentage
Regression Model

## Slide 8: Research Area and Kentucky Coal Reserve Map
Research Area Characteristics
Developed= 5%, Agriculture= 1.5%, Grass/Pasture=15.5%, Forest/Woods=76%, Barren=3.5% (2011 NLCD)
1768 km2 (683 sq-mi)
Minimal underground mining (KDMP)
Variety in mining extent and reclamation age (Landsat 5,7,8)

## Slide 9
Vegetation Cover Change Analysis
Landsat
1986, 1990, 1994, 1999, 2002, 2006, 2010, 2014 and 2017
RGB, NIR
NDVI
1986, 1990, 1994, 1999, 2002, 2006, 2010, 2014 and 2017
Reclassification
1986, 1990, 1994, 1999, 2002, 2006, 2010, 2014 and 2017
Barren, Grass, Woods, Forest
Earth Explorer | Image Analysis | Reclassify tool | Raster Calculator | Cell Statistics | Con Tool | Zonal Histogram | Table to Excel | SPSS

## Slide 10
May 15 Field study (n=9)
Jul 21 Field study (n=15)
Oct 21 Field study (n=58)
Laboratory analysis
Laboratory analysis
In situ measurements
SO42-, alkalinity, conductivity, Ca2+, Mg2+, Mn, Al, and Fe
SO42-, alkalinity, conductivity, Ca2+, Mg2+, Mn, Al, and Fe
Dependent variables
Dependent variables
Dependent variable
Conductivity
Sampling and measurement
NHD 100k stream shapefile
HUC10 basin polygons
Stream reach watershed polygons
Water Quality Analysis

## Slide 11
Mining (%) vs Conductivity (uS/cm)
R= 0.86; P<0.01
N=58, October 21

## Slide 12
Reclaimed Forest (%) vs Conductivity (uS/cm)
R= -0.07; P> 0.05
N=58, October 21

## Slide 13
Mining-RF (%) vs Conductivity (uS/cm)
R= 0.90; P<0.01
N=58, October 21

## Slide 14
Reclamation Age vs Conductivity (uS/cm)
R= -0.67; P<0.01
N=58, October 21

## Slide 15
Pearson Correlation Matrix (May 15, 2017 n=9) |  |  |  |  |  |  |  |  |  | 
 | Mined (%) | Mined w/o RF (%) | Reclaimed Forest (%) | Reclaimed Woods (%) | Reclamation Age (Years) | Alkalinity (mg/L) | Conductivity (uS/cm) | SO42- (mg/L) | Ca2+ (mg/L) | Mg2+ (mg/L)
Mined (%) | 1 | .980** | .886** | .920** | .255 | .751* | .761* | .749* | .776* | .791*
Mined w/o RF (%) | .980** | 1 | .775* | .940** | .155 | .785* | .794* | .775* | .797* | .837**
Reclaimed Forest (%) | .886** | .775* | 1 | .726* | .443 | .553 | .563 | .568 | .601 | .558
Reclaimed Woods (%) | .920** | .940** | .726* | 1 | .338 | .907** | .884** | .843** | .903** | .914**
Reclamation Age (Years) | .255 | .155 | .443 | .338 | 1 | .241 | .158 | .182 | .218 | .159
Alkalinity (mg/L) | .751* | .785* | .553 | .907** | .241 | 1 | .985** | .897** | .993** | .962**
Conductivity (uS/cm) | .761* | .794* | .563 | .884** | .158 | .985** | 1 | .933** | .987** | .969**
SO42- (mg/L) | .749* | .775* | .568 | .843** | .182 | .897** | .933** | 1 | .921** | .964**
Ca2+ (mg/L) | .776* | .797* | .601 | .903** | .218 | .993** | .987** | .921** | 1 | .974**
Mg2+ (mg/L) | .791* | .837** | .558 | .914** | .159 | .962** | .969** | .964** | .974** | 1
**. Correlation is significant at the 0.01 level (2-tailed). |  |  |  |  |  |  |  |  |  | 
*. Correlation is significant at the 0.05 level (2-tailed). |  |  |  |  |  |  |  |  |  | 

## Slide 16
Pearson Correlation Matrix (July 21, 2017 n=15) |  |  |  |  |  |  |  |  |  | 
 | Mined (%) | Mined w/o RF (%) | Reclaimed Forest (%) | Reclaimed Woods (%) | Reclamation Age (Years) | Alkalinity (mg/L) | Conductivity (uS/cm) | SO42- (mg/L) | Ca2+ (mg/L) | Mg2+ (mg/L)
Mined (%) | 1 | .956** | .280 | .780** | -.407 | .457* | .790** | .777** | .795** | .754**
Mined w/o RF (%) | .956** | 1 | -.013 | .705** | -.626** | .581** | .899** | .891** | .904** | .879**
Reclaimed Forest (%) | .280 | -.013 | 1 | .352 | .665** | -.344 | -.251 | -.269 | -.249 | -.308
Reclaimed Woods (%) | .780** | .705** | .352 | 1 | -.240 | .287 | .550** | .467* | .486* | .474*
Reclamation Age (Years) | -.407 | -.626** | .665** | -.240 | 1 | -.478* | -.702** | -.712** | -.702** | -.715**
Alkalinity (mg/L) | .457* | .581** | -.344 | .287 | -.478* | 1 | .693** | .640** | .679** | .723**
Conductivity (uS/cm) | .790** | .899** | -.251 | .550** | -.702** | .693** | 1 | .983** | .990** | .988**
SO42- (mg/L) | .777** | .891** | -.269 | .467* | -.712** | .640** | .983** | 1 | .994** | .991**
Ca2+ (mg/L) | .795** | .904** | -.249 | .486* | -.702** | .679** | .990** | .994** | 1 | .988**
Mg2+ (mg/L) | .754** | .879** | -.308 | .474* | -.715** | .723** | .988** | .991** | .988** | 1
**. Correlation is significant at the 0.01 level (2-tailed). |  |  |  |  |  |  |  |  |  | 
*. Correlation is significant at the 0.05 level (2-tailed). |  |  |  |  |  |  |  |  |  | 

## Slide 17
 | Pearson Correlation Matrix (Oct 11, 2017 n=58) |  |  |  |  |  | 
 | Mined (%) | Reclaimed Forest (%) | Reclaimed Woods (%) | Reclamation Age (year) | Conductivity (uS/cm) | Log Mined | Mined w/o RF (%)
Mined (%) | 1 | 0.223 | .831** | -.496** | .863** | .908** | .965**
Reclaimed Forest (%) | .223 | 1 | .246 | .500** | -0.072 | .451** | -.032
Reclaimed Woods (%) | .831** | .246 | 1 | -.329* | .720** | .796** | .799**
Reclamation Age (year) | -.496** | .500** | -.329* | 1 | -.672** | .294* | .636**
Conductivity (uS/cm) | .863** | -.072 | .720** | -.672** | 1 | .726* | .904**
Log Mined | .908** | .451** | .796** | .294* | .726** | 1 | .823**
Mined w/o RF (%) | .965** | -.032 | .799** | .636** | .904** | .823** | 1
**. Correlation is significant at the 0.01 level (2-tailed). |  |  |  |  |  |  | 
*. Correlation is significant at the 0.05 level (2-tailed). |  |  |  |  |  |  | 

## Slide 18
 | Minimum | Mean | Maximum
Mined (%) | 2.52 | 38.09 | 92.23
Reclaimed Forest (%) | 0.42 | 8.21 | 30.41
Reclaimed Woods (%) | 1.27 | 17.42 | 44.01
Reclamation Age (year) | 4.12 | 15.99 | 27.95
Mined w/o RF (%) | 2.10 | 29.88 | 90.92
Conductivity (uS/cm) | 120.00 | 763.10 | 1970.00
Descriptive Statistics
Only 21% of mined area on average was converted to reclaimed forest between 1986 to 2017.
Conductivity >300 uS/cm affects aquatic environment negatively (Bernhardt et al. 2011; Griffith et al. 2012). 72% of the watersheds had conductivity >300 uS/cm
Conductivity >500 uS/cm indicates ecological impairment and decreases biological diversity (Agouridis et al. 2012; Pond et al. 2008). 55% of watersheds had conductivity >500 uS/cm.

## Slide 19: Effects of mined and reclamation age parameters on conductivity
Regression Model A Summary –Conductivity Prediction |  |  |  | 
Step | R | R2 | R2 adj | Δ R2
Mining Percentage | .863a | .745 | .741 | .745
Reclamation Age | .908b | .825 | .818 | 0.08
Coefficients for Final Model |  |  | 
 | B | β | p
(Constant) | 610.732 |  | <.001
Mining Percentage | 16.956 | .703 | <.001
Reclamation Age (year) | -30.860 | -.324 | <.001
Hypothesis: No significant correlation between mining percentage, reclamation age, and water quality parameters in watersheds mined between 1986 to 2017
Other studies reported conductivity was best predicted with mining percentage (Hopkins et 2013; Merriam et al 2015; Bernhardt et al. 2012)
  None of these studies reported a correlation between reclamation age and conductivity.
In this study, reclamation age was a significant contributor in conductivity prediction

## Slide 20: Effects of vegetation cover change on conductivity
Regression Model B Summary – Conductivity Prediction |  |  |  | 
Step | R | R2 | R2 adj | Δ R2
Mined w/o RF (%) | .904 | .816 | .813 | .816
Reclamation Age (years) | .912 | .832 | .826 | .016
Coefficients for Final Model |  |  | 
Model | B | β | p
(Constant) | 429.20 |  | <.006
Mined w/o RF (%) | 19.54 | .799 | <.001
Reclamation Age (years) | -15.64 | -.164 | <.026
Hypothesis: Reclaimed forest or reclaimed woods do not affect CMRWQ in watersheds
Removing the reclaimed forested areas suggests that reclaimed forest has a positive effect on conductivity mitigation (Wei et al. 2011).
This model indicated that the model improved slightly on the prediction of conductivity.

## Slide 21: Conclusion
Conductivity was highly associated with other coal mine water quality parameters (alkalinity, SO42-, Ca2+, Mg+2) except Al, Fe.
Mining percentage (1986-2017) inversely related with water quality.
There was a moderate but significant correlation between reclamation age and water quality.
Accounting vegetation cover change (reclaimed forest areas) improved the conductivity prediction.

## Slide 22: Acknowledgments & Thanks
This research is funded by USDA / NIFA “Enhancing Research-and-Extension Capability by Studying Land Cover Change, Quality of Life, and Microclimate Variation in Kentucky.” Award Number: 2014-38821-22398, Kentucky State University (PI Dr. Buddhi Gyawali).
This research was funded by USDA Forest Service McIntire Stennis grant- Geospatial Characterization of Kentucky Forests for Agroforestry and Bioenergy Production” 2013-2017, Grant Number 210165 (PI Dr. Kirk Pomper).
Dr. Buddhi Gyawali, Dr. George Antonious, Dr. Ken Semmens, Dr. Demetrio Zourarakis
Jeremy Sandifer, Ken Bates and Dr. Tilak Shresta, Laura Rogers, Ralph Rogers
Marty Matisoff and Dr. Christina McManus
Jarod Jones, Gabriel Stone and Sujan Bhattarai
Dr. Carmen Agouridis, Chris Osborne and University of Kentucky Robinson Forest
Kentucky State University College of Agriculture, Food Science and Sustainable Systems.

## Slide 23
Agouridis, C. T.; P. N. Angel; T. J. Taylor; C. D. Barton; R. C. Warner; X. Yu & C. D. Wood (2012). Water quality characteristics of discharge from reforested loose-dumped mine spoil in eastern Kentucky. Journal of Environmental Quality 41: 454–468.
Bernhardt, E. S.; B. D. Lutz; R. S. King; J. P. Fay; C. E. Carter; A. M. Helton ... & J. Amos (2012). How many mountains can we mine? Assessing the regional degradation of central Appalachian rivers by surface coal mining. Environmental science & technology, 46(15), 8115-8122.
Energy and Environment Cabinet (EEC) (2016). History of Coal in Kentucky, http://energy.ky.gov/Coal%20Facts%20Library/Kentucky%20Coal%20Facts%20-%2016th%20Edition%20(2016).pdf, Accessed on Aug 19, 2017
Evans, D. M.; C. E. Zipper; E. T. Hester & S. H. Schoenholtz (2015). Hydrologic effects of surface coal mining in Appalachia (US). JAWRA Journal of the American Water Resources Association, 51(5), 1436-1452.
Griffith, J. A. (2002). Geographic techniques and recent applications of remote sensing to landscape-water quality studies. Water, Air, & Soil Pollution, 138, 181−197.
Hopkins, R. L.; B. M. Altier; D. Haselman; A. D. Merry & J. J. White (2013). Exploring the legacy effects of surface coal mining on stream chemistry. Hydrobiologia, 713(1), 87-95.
Hooke, R. (1999). Spatial distribution of human geomorphic activity in the United States: comparison with rivers. Earth Surface Processes and Landforms, 24(8), 687-692.
Lindberg, T. T.; E. S. Bernhardt; R. Bier; A. M. Helton; R. B. Merola; A. Vengosh & R. T. Di Giulio (2011). Cumulative impacts of mountaintop mining on an Appalachian watershed. Proceedings of the National Academy of Sciences, 108(52), 20929-20934.
Merriam, E. R.; J. T. Petty; M. P. Strager; A. E. Maxwell & P. F. Ziemkiewicz (2015). Landscape-based cumulative effects models for predicting stream response to mountaintop mining in multistressor Appalachian watersheds. Freshwater Science, 34(3), 1006-1019.
Merricks, T. C.; D. S. Cherry; C. E. Zipper; R. J. Currie & T. W. Valenti (2007). Coal-mine hollow fill and settling pond influences on headwater streams in southern West Virginia, USA. Environmental Monitoring and Assessment, 129(1-3), 359-378.
Key References

## Slide 24
Negley, T. L. & K. N. Eshleman (2006). Comparison of stormflow responses of surface mined and forested watersheds in the Appalachian Mountains, USA. Hydrological Processes, 20, 3467−3483.
Palmer, M. A.; E. S. Bernhardt; W. H. Schlesinger; K. N. Eshleman; E. Foufoula-Georgiou; M. S. Hendryx ... & P. S. White, (2010). Mountaintop mining consequences. Science, 327(5962), 148-149.
Petty, J. T.; J. B. Fulton; M. P. Strager; G. T. Merovich Jr; J. M. Stiles & P. F. Ziemkiewicz (2010). Landscape indicators and thresholds of stream ecological impairment in an intensively mined Appalachian watershed. Journal of the North American Benthological Society, 29(4), 1292-1309.
Phillips, J. D. (2004). Impacts of surface mine valley fills on headwater floods in eastern Kentucky. Environmental Geology, 45(3), 367-380.
US EPA (2011). In The Effects of Mountaintop Mines and Valley Fills on Aquatic Ecosystems of the Central Appalachian Coalfields; EPA/600/ R-09/138F; U.S. Environmental Protection Agency: Washington, DC, 2011.
US EPA (2013). Enviro-atlas, Hydrologic Unit Codes https://enviroatlas.epa.gov/enviroatlas/DataFactSheets/pdf/Supplemental/HUC.pdf Accessed on Feb 12, 2018
Wei, X.; H. Wei & R. C. Viadero Jr (2011). Post-reclamation water quality trend in a Mid-Appalachian watershed of abandoned mine lands. Science of the Total Environment, 409(5), 941-948.
Zipper, C. E.; J. A. Burger; J. G. Skousen; P. N. Angel; C. D. Barton; V. Davis & J. A. Franklin (2011). Restoring forests and associated ecosystem services on Appalachian coal surface mines. Environmental Management, 47(5), 751-765.
Key References

## Slide 25: Thank you! QUESTIONS & COMMENTS

## Slide 26: Limitations & Future Studies
Regression Model A and B are specific to impacted areas with a low proportion of developed and agricultural lands, although this situation is common in central Appalachia.
Temporal and spatial bias on reclamation age and delineated mined areas. Most of the active areas, however, overlapped between time intervals.
Vegetation cover change conductivity examination can be repeated using more reliable data to improve the prediction models.
Future studies may possibly include underground mining, developed areas and agricultural area effects with increased sample size.

## Slide 27
Linear
Independent variables
Normal distribution
Normal
Not normal
Linearity check
Transformation
Dependent variables
Normal distribution
Not normal
Normal
Transformation
Normal
Not normal
Not normal
Normal
Not linear
Variable removed
Variable removed
Transformation
Bivariate Pearson Correlation
P > 0.05
P ≤ 0.05
No significant relation between variables
Multivariate Regression Model
Multivariate Regression Model Equation
Y = β0+ β1 XI +……..+ βnXn + e
Removing insignificant coefficients, collinear variables and checking heteroscedasticity
Not linear
Variable adjusted
Statistical Analyses

## Slide 28
Appendix 1. Example calculations for used equations in vegetation cover analysis
2000.66 =
16.34 = 2017-2000.66
*100
*100
*100

## Slide 29
r
Calculation of Remote Sensing Variables
Undisturbed
Active
Mined in 1986, now reclaimed Forest

## Slide 30
 |  |  | Conductivity |  |  | 
Watershed | Mined-RF | Rec. Age | 15-May | 21-Jul | 21-Oct | 
9 | 9.05 | 20.3 | 88 | 203 | 190 | 
10 | 11.53 | 18.47 | 165 | 279 | 270 | 
11 | 21.97 | 22.1 | 176 | 348 | 310 | 
29 | 32.99 | 21 | 280 | 627 | 560 | 
32 | 7.71 | 14.24 | 130 | 174 | 160 | 
33 | 18.28 | 16.45 | 153 | 245 | 210 | 
34 | 12.62 | 21.62 | 120 | 266 | 190 | 
ANOVA |  |  |  | 
source | df | SS | MS | F
Total N | 20 | 0.000103 |  | 
Group | 2 | 4.23E-05 | 2.11E-05 | 6.292259
Error | 18 | 6.05E-05 | 3.36E-06 | 
F > F(2,18) Then p < 0.05
Appendix 5. Seasonal conductivity change

## Slide 31
ReclaimedGrass
Appendix 6. Vegetation Cover Change Analysis
Reclaimed
Woods
Reclaimed
Forest
Active
Mining
Unmined

## Slide 32
FeS2 + 3.75O2 + 3.5H2O → Fe(OH) 3 + 2SO42- + 4H+
2CaCO3 + 2H+ → Ca2+ + 2HCO3- CaMgCO3 + 2H+ → Ca2+ +Mg2+ + 2HCO3-
FeCO3 + 2H+ → Fe2+ + 2HCO3-
Major inorganic minerals in coal are: quartz (SiO2), clay minerals (contain Al and (OH)), pyrite (Fe2S), calcite (CaCO3), siderite (FeCO3).
Appendix 7. Major elements and minerals found in coal

## Slide 33
Appendix 8. 2011 NLCD Land cover classes

## Slide 34: References

## Slide 35: References

## Slide 36: References