## Slide 1: Ascertaining the Effects of Gaseous Pore Pressure and Net Confining Stress on Permeability of Tight Cores Using a New Steady-State Approach
Michael J. Hannon, Jr.* - Indiana Geological and Water Survey
Yael T. Tucker – National Energy Technology Laboratory, ORISE
Daniel J. Soeder – South Dakota School of Mines & Technology

## Slide 2: Shale Oil & Gas Recovery
Horizontal Well
Hannon, M.J. & S. Finsterle. The Effect of Anisotropy on Multi-dimensional Pressure-Pulse-Decay Experiments. Transport in Porous Media (2018). 123:545–562. https://doi.org/10.1007/s11242-017-0941-x
1
2
3
Time
Recovery Rate
Darcy/turbulent fracture flow
Gas desorption
Darcy matrix flow
Recovery Mechanisms:
** Large pressure gradients near fractures due to low permeability

## Slide 3: Permeability Enhancement at Lower Pore Pressure (Gas Slip or “Klinkenberg” Effects)
  – Intrinsic permeability (m2)
  – Klinkenberg coefficient (Pa)
Permeability to gas increases at lower pore pressure
Enhanced at smaller pore diameters (i.e., lower permeabilities)
Could even include sorption processes
Klinkenberg, L.J. The Permeability of Porous Media to Liquids and Gases. In Drilling and Production Practice (1941), pp. 200-213.

## Slide 4: Permeability Reduction at Lower Pore Pressure (Net Effective Stress)
  – Unconfined permeability (m2)
  – Confining-stress decay constant (Pa-1)
  – Net confining stress deviation factor (-)
Permeability to gas decreases at lower pore pressure (higher net effective stress)
Enhanced with less stiff (compressible) materials (i.e., more clays)
Hysteresis
Yang, Y. and A.C. Aplin. Permeability and Petrophysical Properties of 30 Natural Mudstones. Journal of Geophysical Research (2007), 112:B03206.

## Slide 5: The Randolph Steady-State Core Analysis Laboratory (RaSSCAL)
Core Sample
Upstream (u)
Downstream (d)
Quasi steady-state permeability assessment
Modified for high pressure gradients
  Faster flow through the sample
  More similar to in-situ conditions
  Math becomes trickier
u
d
Core Sample
p
t
pd
pu
Similar to WVU PPAL system. See Zamirian et al. New Steady-State Technique for Measuring Shale Core Plug Permeability. From SPE/CSUR Unconventional Resources Conference (2014), SPE-171613-MS. https://doi.org/10.2118/171613-MS

## Slide 6: Standard Darcy’s Law
Standard form of Darcy’s Law
Does not account for gas density, viscosity, or compressibility changes.
Does not account for general permeability changes with pressure (Klinkenberg and net stress effects discussed earlier).
Useful for small pressure ranges.
u
d
Core Sample
p
t
pd
pu

## Slide 7: Fancy Darcy’s Law
Expanded form of Darcy’s Law
Accounts for gas density, viscosity, and compressibility changes over arbitrary pressure ranges.
  evaluated for each gas using NIST REFPROP database.
Accounts for gas slip and net effective stress by superposition of previous relationships
u
d
Core Sample
p
t
pd
pu

## Slide 8: Results – Marcellus Shale
– Unconfined intrinsic permeability (m2)
– Confining-stress decay constant (Pa-1)
– Klinkenberg coefficient (Pa)
– Net confining stress deviation factor (-)
Methane:
= 212 nd, = 128 psi, = 0.152 MPa-1, = 0.315
Helium:
= 398 nd, = 745 psi, = 0.166 MPa-1, = 0.055

## Slide 9: Results – Oriskany Sandstone
Methane:
= 41 nd, = 0 psi, = 0.046 MPa-1, = 4.8
Helium:
= 117 nd, = 0 psi, = 0.081 MPa-1, = 2.182
– Unconfined intrinsic permeability (m2)
– Confining-stress decay constant (Pa-1)
– Klinkenberg coefficient (Pa)
– Net confining stress deviation factor (-)

## Slide 10: Future Work
More comprehensive data set needed
More comprehensive models:
    Covers poro-elastic effects*
  Transitional regime (Kn > 0.1)
  More parameters = more data
Upgrades to the experimental apparatus
  Automatic syringe pump rather than large volumes for pressure control
  Trigger “RaSSCAL” approach when flow rates are too low to measure directly
*Fink et al. Apparent permeability of gas shales – Superposition of fluid-dynamic and poro-elastic effects. *Fuel (2017). 199:532–550. https://doi.org/10.1016/j.fuel.2017.02.086
Core Holder
H
L
DP Transmitter
From Pump
Const.
Pressure
Thanks for your time!
Any questions?