## Slide 1: Climate change effects over Belo Monte Dam’s hydroelectricity generation capacity: economic, environmental and social impacts
Marcelo G. P. Camargo (University of São Paulo - Brazil)
Prof. Dr. André O. Sawakuchi (USP - Brazil)
Prof. Dr. Gyrlene A. M. Silva (UNIFESP - Brazil)
Prof. Dr. Victor Sacek (USP - Brazil)
Grant 2017/12470-2
Photo: Betto Silva

## Slide 2: Context
Radar image - Jan/2016
Credits: Juan Doblas/ISA

## Slide 4
Belo Monte
Pimental
Photos: André Sawakuchi
Artificial reservoir level
Xingu River (Stretch of Reduced Inflow)
Main powerhouse
Installed turbines (4 of 18 as of 2016)
~ 90 m
Xingu River reservoir level
Xingu River
Closed doors
~ 20 m

## Slide 5: Belo Monte Dam – Main features
(Norte Energia, 2016)
Run of the river-type Dam
Reduced reservoir area
Generation capacity ≈ river’s discharge

## Slide 6
~ 100% installed capacity
Severely reduced to non-existant generation

## Slide 7: Objective Evaluate Belo Monte’s energy generation potential over the next 30 years through simulations of Xingu River’s future discharge

## Slide 8: Motivation
(Sorribas et al., 2016)
Projections from five CMIP5/IPCC GCMs regarding surface water availability by the end of the century

## Slide 9: Method – Hydrologic simulation
ETOPO1 Digital Elevation Model
Drainage system calculation based on topographic gradients
(Amante and Eakins, 2009)

## Slide 10
SRTMs:
25_13, 14 e 15
26_13, 14 e 15
(Datum: WGS84)
(Camargo et al., in prep.)

## Slide 11
Results

## Slide 12: Numeric model calibration through historical rainfall data
To better simulate rainfall loss due to water percolation / ET, only 30% of total rainfall contributed to the discharge
*
*das diferenças entre cada valor simulado e observado

## Slide 13: Future rainfall projections (multi-model average)
Persistent negative anomalies might be significantly worse to the river’s water availability than just one very negative anomaly

## Slide 14: Discharges (2017 – 2045)
Average high water discharge (1971-2014)
-40%
Total discharge needed to fully operate while releasing water to the Stretch of Reduced Inflow.

## Slide 15
Future discharges are expected to be on average 28% lower than the historical ones

## Slide 16
Discussion
Effects of deforesting on Xingu’s discharge
Present and future impacts of Belo Monte

## Slide 17
Projections of forest area loss at the Xingu River’s Basin by 2099, considering three scenarios of change on land use
(Adaptado de Guimberteau et al., 2016)
Foto: André Sawakuchi

## Slide 18
ET reduction only
Considering changes in rainfall
(Adaptado de Guimberteau et al., 2016)
Effects of deforesting on Xingu River’s discharge
(Stickler et al., 2013)

## Slide 19
Changes on Amazonian rivers’ mean discharges (2070 – 2099)
(Sorribas et al., 2016)
Other papers point out similar (or even worse) scenarios, that will persist through Belo Monte’s entire estimated life

## Slide 20: Solution: building more dams?
National Energy Policy Council Resolution – nº 6, 03/Jul/2008
Determines that the only comercially explored hydroelectric potential of the Xingu River is supposed to be Belo Monte
Very significant environmental impacts to:
Local population, biodiversity and ecosystems
Fotos: Rodolfo Salm e Marcelo Camargo

## Slide 21
Final remarks

## Slide 22
The hydrologic model precisely simulated historical discharges, showing to be a valid method;
Climatic projections point out less rainfall in the next few decades, compared to historical average;
Future simulated discharges are in average 28% lower than the historical means, which is in consonance with recent studies that predict a significantly drier in Eastern Amazon;
A future lower water availability will imply the decreasing of Belo Monte’s energy production;
Other energy resources present higher cost-benefits while also being notedly less impactul as hydropower in Amazon.

## Slide 24
Obrigado!
Thank you!
Marcelo Camargo
Graduate Student (USP – Brazil)
marcelogpcamargo@gmail.com
Foto: Marcelo Camargo

## Slide 25: References
Amante, C., B.W. Eakins (2009). ETOPO1 1 Arc-Minute Global Relief Model: Procedures, Data Sources and Analysis. NOAA Technical Memorandum NESDIS NGDC-24. National Geophysical Data Center, NOAA.
de Jong, P., Kiperstok A., Torres E.A. (2015). Economic and environmental analysis of electricity generation technologies in Brazil. Renewable and Sustainable Energy Reviews, 52, 725–739.
Dias, L. C. P., Macedo, M. N., Costa, M. H., Coe, M. T., Neill, C. (2015). Effects of land cover change on evapotranspiration and streamflow of small catchments in the Upper Xingu River Basin, Central Brazil. J. Hydrology: Regional Studies, 4 (B), 108-122.
Garcia-Castellanos, D. (2002). Interplay between lithospheric flexure and river transport in foreland basins. Basin Research, 14(2), 89-104.
Guimberteau et al. (2016) Impacts of future deforestation and climate change on the hydrology of the Amazon basin: a multi-model analysis with a new set of land-cover change scenarios. Hydrol. Earth Syst. Sci. Discuss. Em revisão.
IPCC (2014). Climate Change 2014: Synthesis Report. Contribution of Working Groups I, II and III to the Fifth Assessment Report of the Intergovernmental Panel on Climate Change. [Pachauri, R. K., Meyer, L. A. (eds.)]. IPCC, Geneva, Switzerland. http://www.ipcc.ch/report/ar5/index.shtml. Acesso em 22/02/2016.
Norte Energia S.A. (2016). UHE Belo Monte. <http://norteenergiasa.com.br/revista/>. Acessado em 20/07/2016.
Sacek, V. (2011). Modelagem numérica conjunta de processos sedimentares e tectônicos em bacias sedimentares. Tese de doutorado, IAG – USP.
Sacek, V. (2014). Drainage reversal of the Amazon River due to the coupling of surface and lithospheric processes. Earth and Planetary Science Letters, 401, 301-312.
Sorribas, M. V., Paiva, R. C. D. et al. (2016). Projections of climate change effects on discharge and inundation in the Amazon basin. Climatic Change, 136, 555-570.
Stickler, C. M., Coe, M. T., Costa, M. H., Nepstad, D. C., McGrath, D. G., Dias, L., Rodrigues, H. O., Soares-Filho, B. S. (2013). Dependence of hydropower energy generation on forests in the Amazon Basin at local and regional scales. Proceedings of The National Academy of Sciences, 110 (23), 9601-9606.
Vuuren, D. P., Edmonds, J., Kainuma, M. et al. (2011). The representative concentration pathways: an overview. Climatic Change, 109:5