## Slide 1
Interactions between Groundwater and Surface Water at a Mid-Upper Reach of the Yadkin River
and Their Implications in Nutrients Loading to the River from Residuals Land Application Fields
Shuying Wang1, Angela M. Moore2, Chuanhui Gu3
1North Carolina Division of Water Quality, Raleigh, 27601, NC; 2Department of Geology, Guilford College, Greensboro, NC 27410; 3Department of Geology, Appalachian State University, Boone, NC 28607
2012 GSA, Charlotte
Purpose of Investigation
This investigation was launched in May 2011 to help the N.C. Division of Water Quality (DWQ) determine if the current rules and monitoring requirements for residuals land application permits are adequate to protect the quality of ground and surface waters of North Carolina and if groundwater discharge is a significant source of nutrient loading to surface water from residuals land application fields.
Methods of Investigation
Water chemistry analysis: The Yadkin River and monitoring wells have been sampled three times for laboratory analyses of TOC, DOC, nutrients, trace metals, and major ions. pH, DO, and specific conductance were measured in the field when samples for laboratory analyses were collected. Mid- and up-streams of the two creeks and some piezometers were sampled only once for select parameters.
Horizontal hydraulic conductivity determination: Rising and/or falling head slug tests were performed at each well to assess the horizontal hydraulic conductivity of the aquifer tapped by the wells. The slug-test data were analyzed using the Bouwer and Rice (1976) method spreadsheet developed by Halford and Kuniansky (2002).
Hydraulic gradient and water flow were analyzed through water level monitoring. Groundwater and stream stage were monitored with either YSI Level Scout® or HOBO U20 Water Level Loggers. Data were recorded either hourly or every 20 minutes.
Water temperature measurements: Water temperature data were collected along transects crossing the riparian zone from inland to the Yadkin River with Tidbit v2 Water Temperature Loggers and YSI and HOBO water level loggers.
Based on the groundwater flow calculated above and the average nitrate concentration (8.7 mg/L) within the riparian-hyporheic zone, it is estimated that each year about 29.5 kg of nitrogen
{[Q (9288 L/day) x N concentration (8.7 mg/L)] x 365 day /106}
discharged/discharges through the vertical plane of the reach of the Yadkin River between the two creeks from the study field to the Yadkin River through groundwater discharge.
Acknowledgements
We thank Sherri Knight, the supervisor of NC DWQ Aquifer Protection Section and her staff members for their support and assistance on field investigation. We also thank the property owner for allowing us to investigate the field and their passion in cooperation with this investigation.
For more information
Shuying Wang, shuying.wang@ncdenr.gov, Winston-Salem Regional Office (336) 771-5000
Conclusions
Field observations coupled with laboratory analysis results suggest that denitrification may be able to reduce ~80% of nitrate present in groundwater as it flows through riparian-hyporheic zones (from 37.33 mg/L at MW-5 to 7.6 mg/L at PZ-1). The reduction of nitrate occurred in the last few feet of stream sediment, from 7.6 mg/L at PZ-1 and 2.0 mg/L at CPZ-1S, is probably due to the exchange of groundwater and surface water or dilution from the Yadkin River.
Under baseflow conditions, groundwater discharges into the river through the vertical plane of the reach between the two creeks at an estimated flow rate of 328.57 ft3/day; an estimate of 29 kg of nitrate discharges into the Yadkin River through groundwater discharge through the river bank each year under current site conditions.
More studies including small scale and more intensive water quality sampling need to be conducted. Discharges at both upstream and downstream of the reach should be measured, and streambed seepage rates should be tested to quantity if groundwater discharge is a significant source of nutrient loading to surface water from residuals land application fields.
Results
The investigation found that elevated nitrate levels were detected in groundwater throughout the studied site. However, it decreased across the riparian zone. Groundwater generally perpendicularly flows from the field to the Yadkin River (Fig. 2).
Fig. 2. shows shallow groundwater flow direction and concentrations of nitrate in groundwater and surface waters. Nitrate concentrations in two side creeks are similar to those in groundwater and much higher under baseflow than under stormflow conditions. For instance, nitrate was detected at SW-E-M at 19 mg/L under a baseflow condition, but only 4.2 mg/L was detected during a storm event.
Description of the Study Site
The site is an agricultural field moderately sloping from low terrace into floodplain adjacent to a mid-upper reach of the Yadkin River and bordered by unnamed creeks on two sides. The study field (LP-25) had received industrial wastewater treatment residuals for 18 years, but in the past five years no residuals were applied. Upgradient fields still receive residuals applications twice a year. Corn has been growing each year for many years in the study field and adjacent upgradient fields. For this study, a total of thirteen monitoring wells including five piezometers were installed at select locations and designed depths throughout the field and along the reach of the Yadkin River (Fig. 1).
The streambed or hyporheic zone is a great buffer for temperature: the streambed temperature was higher than the channel temperature during cold weather but lower than the channel temperature during summer (Fig. 9). Data also shows a gaining condition during summer season.
Fig. 1. Site map showing locations of wells and surface waters, North Carolina, Wilkes County
Fig. 4 Changes in pH, dissolved oxygen and specific conductance in water across riparian zone. Ground water is mixed in this zone, and hyporheic zone (CPZ-1S) is highly affected by surface water.
Chart: pH Value
| MW-5 | MW-9 | PZ-1 | CPZ-1S | CPZ-1
pH-Field | 5.3467 | 5.53 | 5.81 | 6.02 | 6.29
Chart: Dissolved oxygen, mg/L
| MW-5 | MW-9 | PZ-1 | CPZ-1S | CPZ-1
Dissolved Oxygen (mg/l) | 5.55 | 2.85 | 3.08 | 4.71 | 9.4275
Chart: Specific conductance, uS/cm
| MW-5 | MW-9 | PZ-1 | CPZ-1S | CPZ-1
Specific Conductance (us/cm) | 368.9 | 383.3333 | 202 | 122 | 66.175
Water Level measurements and Hydraulic Gradient
Groundwater discharge or surface water flow that passes through the vertical plane of the reach of the Yadkin River between the two creeks can be roughly estimated with the Darcy equation as:
Q = KA(h1-h2)/L
=1.03 ft/day x (1000 ft x 5 ft)(75.30 ft – 72.21 ft)/ 50 ft
= 328.57 ft3/day
= 9288 l/day
where
Q (ft3/day) is flow through a vertical plane that extends beneath the riverbank;
K is horizontal hydraulic conductivity (1.03 ft/day) estimated from the onsite slug tests
A is the area of the plane through which groundwater passes to enter into the Yadkin River;
h1 is 75.30 ft, the average hydraulic head of three monitoring wells;
h2 is 72.21 ft, the average surface water stage of three surface-water stage measure points;
and, L is 50 ft, average distance from monitoring wells to the riverbank.
Chart: Relative elevation of water surface (ft)
Chart: Date/time data recorded
Fig. 5. Fluctuations of groundwater table vs. stream
stage due to precipitations
Fig. 7. Groundwater temperature in monitoring well MW-4
more than 50 feet away from the Yadkin Rive lagged
the river temperature at CPZ-3 by about four months
Chart: Temperature (F)
Chart: Temperature (F)
Date/time data recorded
Fig. 9. CPZ-S = temperature measured at 1 ft below the surface of streambed; CPZ-1 = bottom of channel water; MW-9 = within the riparian zone; PZ-1 = between MW-9 and CPZ-1S
(67.33)
(22.33)
SW-W-Up
(17.00)
SW-W-M
(15.00)
(25.67)
SW-W
(12.00)
(0.73)
(9.80)
(0.6)
PZ-2 (9.80)
(0.67)
(20.23)
(37.33)
(33.67)
(1.15)
SW-E-M
(19.00/4.2)
PZ-1 (7.60)
CPZ-1S (2.0)
SW-E (15.00)
= Monitoring well/piezometer; = creek sample location; 76.98 = relative water level elevation; (7.60) = nitrate concentration.
Sketches of the Yadkin River and creeks are not accurate or scaled.
Note
pH, Dissolved Oxygen, and Specific Conductance
Fig. 3. pH and dissolved oxygen are lower in groundwater and higher in the Yadkin River. Increase in pH or DO promotes the removal of dissolved metals from groundwater before discharge to the surface water, so specific conductance is much lower in the Yadkin River. Two creeks reflect groundwater.
Chart: Sample ID
| MW-1 | MW-2 | MW-3 | MW-4 | CPZ-3 | MW-5I | MW-5 | MW-9 | PZ-1 | CPZ-1S | CPZ-1 | MW-6 | PZ-2 | CPZ-2 | MW-7 | MW-7I | MW-8 | SW-E-Up | SW-E-M | SW-E | SW-W | SW-W-M | SW-W-Up
Sp. Conductance | 601.5 | 219.6667 | 40 | 369.7667 | 51.2 | 325.2333 | 368.9 | 383.3333 | 202 | 122 | 65.5667 | 151.2667 | 182 | 60.5333 | 259.6667 | 160.6667 | 275 | 182 | 235.6 | 225.0333 | 279.6 | 267.4 | 265.9
pH | 4.3633 | 4.43 | 5.83 | 5.3067 | 6.225 | 7.06 | 5.3467 | 5.53 | 5.81 | 6.02 | 6.1833 | 5.67 | 5.63 | 6.2967 | 5.0267 | 6.12 | 5.3933 | 6.2 | 6.14 | 6.41 | 6.295 | 6.93 | 6.54
Dissolved oxygen | 7.6 | 3.2433 | 7.23 | 3.42 | 10.485 | 5.3 | 5.55 | 2.85 | 3.08 | 4.71 | 9.0967 | 1.6867 | 6.64 | 8.7033 | 3.8967 | 2.82 | 6.61 | 7.62 | 7.14 | 7.24 | 8.075 | 8.14 | 7.58
Chart: Hydraulic gradient change between MW-9 and the Yadkin River
Chart: Hydraulic Gradient between MW-4 and the Yadkin River, CPZ-3
Fig. 6. Horizontal hydraulic gradient between groundwater and the Yadkin River (Inverted when stream stage high)
Well ID | Aquifer tested | Screen interval (ft, BGS) | Average K (ft/d) | Comments
MW-1 | Alluvium, rich in clay | 9-19 | 0.20 | Water table below top of screen, only rising head tests were performed
MW-2 | Alluvium, sandy | 5-15 | 2.50 | 
MW-3 | Colluvium, saprolite | 60-89 |  | Note tested
MW-4 | Alluvium, rich in clay | 6-16 | 2.00 | rising head only
MW-5 | Alluvium | 7-17 | 0.90 | rising head only
MW-5I | Alluvium to dry weathered gneiss | 15-30 | 0.08 | 
MW-6 | Alluvium | 4-21 | 0.40 | 
MW-7S | Alluvium, sandy clay interlayered with silty sand | 3-13 | 1.50 | 
MW-7I | Alluvium, sandy clay interlayered with silty sand | 18-23 | 0.10 | borehole may be smeared.
MW-8 | Alluvium, silty sands | 8-13 | 1.30 | 
MW-9 | Alluvium, silty sands | 6-16 | 0.70 | well may not be well developed
Hydraulic Conductivity and Groundwater Discharge Estimation
Horizontal hydraulic conductivity of alluvial aquifer was estimated from the results of onsite slug tests ranging from 0.2 to 2.5 ft/day. Within the riparian zone, it ranged from 0.7 – 2 ft/day, or 1.03 ft/day on average (Table 1)
Chart: Date/time data recorded
Water Temperature Fluctuation Signals Exchanges
Fig. 8. Groundwater temperatures within the riparian zone near the river have the same trend as the river temperature; piezometer PZ-1 within hyporheic zone was affected more by the river. The river water temperature reflects both daily and seasonal temperature changes.
Table 1. Results of slug tests
Chart: Date/time data recorded