## Slide 1: Use of Radium Isotopes to Evaluate Naturally-occurring Uranium and Radium Sources and Behavior in New Mexico Groundwaters: Examples from Three Sites
May 10, 2012
C.R. Bryan(1), M.D. Siegel(2), D.S. Vinson(3), H. Raanan-Kiperwas(4), A. Vengosh(5), and G.S. Dwyer(5)
Sandia National Laboratories is a multi-program laboratory managed and operated by Sandia Corporation, a wholly owned subsidiary of Lockheed Martin Corporation, for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
(1)Sandia National Laboratories; (2)University of new Mexico; (3)University of Arizona; (4)U.S. EPA Wetlands Division; (5)Duke University

## Slide 2
Outline
In this presentation, we will:
Provide background on U, Th, and Ra geochemistry and Ra isotope occurrence.
Discuss interpretation of variations in isotope occurrence and activity ratios
Discuss analytical methods, concentrating on a relatively new and simple method for assessing groundwater 226Ra and 228Ra concentrations
Present and interpret isotopic data from three New Mexico locations as examples of the use of Ra isotopes to interpret groundwater data

## Slide 3
Background
Elevated levels of uranium and radium are relatively common in New Mexico groundwaters
  Natural enrichments
  Surface and underground mining activities
Groundwater contaminant plumes are difficult and expensive to remediate
  Accurately determining the sources of contamination in groundwater allows apportionment of financial responsibility for remediation costs
U and Ra concentrations and isotope activity ratios:
  provide a useful tool for establishing provenance of groundwater contamination
  provide information on source lithologies and hydrologic conditions, potentially aiding in developing effective treatment strategies

## Slide 4: General geochemistry: U and Th decay chains

## Slide 5: General geochemistry: U and Th decay chains
Half-lives, absolute concentrations, and concentration ratios of decay chain daughter products vary by several orders of magnitude
However, at secular equilibrium, the activities of all daughter radionuclides in a chain will be the same.
Variations in activity ratios (ARs), rather than concentration ratios, provide evidence of disequilibrium, and insights in chemical and physical processes that discriminate between Th and U, or that can separate the different daughters.
Important ratios in these systems are:
  234U/238U
  224Ra/228Ra
  228Ra/226Ra

## Slide 6: Uranium Geochemistry
Uranium behavior in groundwaters is controlled by three major factors: redox condition, complexation in solution, and sorption
Low Eh—U(IV)
  Low solubility (UO2 or coffinite)
  Weakly complexing
Oxidizing conditions—U(VI) (UO22+)
  Much higher solubility
  Forms stable uranyl-carbonato and uranyl-hydroxyl complexes in solution (concentration strongly a function of pH and carbonate concentrations)
Sorption: highly variable, but in general:
  U(IV) sorbs more strongly than U(VI) species
  U sorption decreases in the presence of complexing ligands (carbonate, hydroxyl) or competing cations (Ca, Mg)
  Strongly sorbing minerals include iron oxyhydroxides, carbonate minerals, clays

## Slide 7: Uranium isotope activity ratios
235U/238U — isotopes do not fractionate in nature; significant variations in this ratio are extremely rare (e.g. Oklo)
234U/238U — Secular equilibrium (AR = 1) requires hundreds of thousands of years
  Groundwater 234U/238U AR values are commonly >1.0, and can be >10. 234U enrichment is due to:
    Preferential release of 234U from damaged crystal lattice sites (Slizard-Chalmers effect)
    Alpha recoil—234U or one of its shortlived parents is preferentially ejected from a mineral by radioactive decay processes.
  In stable, near-equilibrium systems,  recoil and preferential dissolution processes dominate, resulting in 234U/238U > 1.0
  In perturbed systems where active U-mineral dissolution is occurring, 234U and 238U are released in proportion to abundance in the rock. Groundwater 234U/238U ARs are close to 1.0. AR values of ~1.0 have been used to source groundwater contamination to uranium mining and storage sites (Rhodes et al., 2006; Zeilinski et al, 2008; Johnson et al., 2009; Otton et al., 2010)

## Slide 8: Radium Geochemistry
Controls on Ra concentration in groundwater:
Abundance of U and Th parents in the source rocks
  Granitic rocks and clasts enriched in U and Th
  U enriched in carbonates, or by post-depositional redox processes in sandstones
  Th enriched in sandstones containing lag concentrations of heavy minerals
Ra geochemistry
  Solubility — low solubility Ra-sulfate; co-precipitation with Ba-sulfate
  Sorption/Ion exchange — Fe, Mn oxyhydroxides and clays
  Aqueous Ra concentrations largely controlled by factors that affect sorption and ion exchange. High Ra generally associated with reduced, acidic, or high ionic strength groundwater (Vengosh et al., 2009; Szabo et al., 2012)
    Redox potential — elevated Ra may be linked to reductive dissolution of Fe, Mn oxides
    pH — affects surface charge of sorbing minerals
    Ionic strength — competition with other cations (Ca, Mg) for sorption sites

## Slide 9: Radium isotope activity ratios: 228Ra/226Ra
  Ra ARs are strongly affected by the balance between alpha recoil processes and removal mechanisms (sorption, precipitation) (Vengosh et al. 2009)
228Ra/226Ra — provides information on Ra sources and aquifer geochemistry
  AR commonly ~ equal to the average Th/U activity ratio in the aquifer rocks (Dickson 1990)
    Igneous rocks: ~1.0–1.4 (crustal average)
    Carbonate aquifers (U-enriched): 228Ra/226Ra <1.0
    Sandstones enriched in U via post-depositional processes (e.g. U roll-front deposits): 228Ra/226Ra <1.0
    Sandstones containing resistate minerals (Th-enriched): 228Ra/226Ra >1.0
  Can deviate from parent ratio in aquifer rocks due to:
    Dissolution of Ra-containing minerals—elevates long-lived relative to short-lived isotope (lower 228Ra/226Ra)
    Alpha recoil processes, coupled with rapid removal (sorption/precipitation)—elevates short-lived relative to long-lived isotope (higher 228Ra/226Ra)

## Slide 10: Radium isotope activity ratios: 224Ra/228Ra
224Ra/228Ra — provides information on residence time, relative importance of sinks vs. alpha recoil
  224Ra/228Ra > 1.0
    Elevated 224Ra/228Ra attributed to alpha-recoil, combined with rapid removal from solution via sorption/precipitation (Szabo et al. 2012)
  224Ra/228Ra ≈ 1.0
    Low sorption, such that the contribution of excess 224Ra due to alpha recoil is small relative to the total Ra in solution (Szabo et al., 2012)
    Exchangeable sorption, such that the sorbed and solution Ra fractions maintain isotopic equilibrium. This requires that the rate of desorption be “…comparable to or greater than the radioactive decay rate of 224Ra and much greater than that of 228Ra” (Krishnaswami et al. 1982)
  224Ra/228Ra < 1.0
    Radium transported far from source

## Slide 11: Methods
RAD-7 radon counter
Delayed coincidence alpha counter
g-spec.
TIMS

## Slide 12: Radium isotope analysis: 223Ra, 224Ra
Determination of radium isotopes (based on methods of Kim et al. 2001 and Moore and Arnold 1996)
223Ra and 224Ra
  Radium quantitatively extracted from 5-20 liters of groundwater by pumping the water through a glass column packed with Mn-oxide coated fibers.
  223Ra and 224Ra determined within 48 hours of collection by counting the fibers with a delayed coincidence alpha counter

## Slide 13: Radium isotope analysis: 226Ra, 228Ra
226Ra
  Following pre-concentration onto the Mn-fibers, the glass filter tubes are purged with He and sealed
  Tubes are allowed to incubate for 3 weeks, to allow ingrowth of 222Rn
  Tubes are hooked to RAD-7 radon analyzer, and the gas is recirculated through the detector. 218Po, the daughter of 222Rn, is collected electrostatically and counted
  226Ra is determined indirectly via 222Rn, in turn determined by counting decay of 218Po
228Ra
  Following 226Ra analysis, Mn-oxide fibers are extracted, dried and crushed into cans
  Cans are counted using -spectrometry. 228Ra is determined indirectly by decay of daughter 228Ac

## Slide 14: Results
Three contrasting sites examined
  Glorieta area
  Four public and private wells
  Completed in Permian sandstones
  Elevated U (8.5–24.2 µg/L), and in one case elevated Ra (up to >14 pCi/L)
  Zuni Mountains area
  Two wells
  One deep well has extremely elevated Ra (>20 pCi/L) and low U
  A nearby, shallower well has low Ra and U
  Laguna area
  Four wells
  Completed in the Jackpile and Brushy Basin members of the Morrison Formation, units which host U roll-front deposits nearby
  Low U and Ra

## Slide 15
Piper Diagram
Glorieta
Zuni-shallow (low Ra)
Zuni-deep (high Ra)
Laguna
Laguna: Na, SO4, HCO3
Glorieta: Ca, Mg, Na,HCO3, Cl
Zuni-shallow: Na, HCO3, SO4
Zuni-deep: Ca, Mg, SO4,HCO3

## Slide 16: Glorieta
Well: | Glorieta Estates | Glorieta MDWA | Private Well A | Private Well B
pH | 7 | 6.96 | 6.79 | 6.74b
DO mg/L | 2.3 | 0.57 | 3.8 | 2.6
NO3 | 10.18 | 1.42 | 48.69 | 16.38
HCO3 | 378 | 354 | 610 | 329
TDS mg/L | 623 | 358 | 648 | 469
223Ra, pCi/L | 0.053 ±0.063 | 0.027±0.020 | 0.019±0.021 | 0.006±0.019
224Ra, pCi/L | 2.15±0.12 | 0.55±0.04 | 1.15±0.06 | 0.63±0.05
226Ra, pCi/L | 6.24±0.27 | 2.91±0.17 | 0.31±0.05 | 0.31±0.05
228Ra, pCi/L | 1.21±0.13 | 0.46±0.09 | 1.02±0.09 | 0.5±0.06
226Ra+228Ra | 7.45 | 3.37 | 1.33 | 0.81
Ra, pCi/L | 9.36 | 3.89 | 2.36 | 1.35
224Ra/228Ra | 1.54 | 1.04 | 0.98 | 1.09
228Ra/226Ra | 0.19 | 0.16 | 3.27 | 1.64
U, µg/L | 15.5 | 8.5 | 24.2 | 21
234U/238U | 1.708±0.0029 | 1.712±0.0051 | 1.629±0.0026 | 2.067±0.0034
  Oxic waters
  Elevated U (8.5–24.2 µg/L)
  228Ra/226Ra AR values vary
  Range of U/Th ratios in aquifer sediments (variable degree of U enrichment?)
  224Ra/228Ra AR ~1.0
  Ra is locally generated
  Ra is labile and aquifer sorptive capacity is low.
  Irreversible removal of Ra (e.g. precipitation) is not important (consistent with low SO4 concentrations)

## Slide 17: Zuni area
  Anoxic
  Well #2: strong enrichment of U in aquifer sediments indicated by:
  Extremely elevated Ra (>20 pCi/L), mostly 226Ra
  Very low 228Ra/226Ra AR values (<0.1)
  U concentrations are low, probably limited by solubility of U(IV) species
  Well #1: enrichment of U in aquifer sediments indicated by low 228Ra/226Ra
Well: | Well #1* | Well #2*
pH | 9.01 | 7.04
DO mg/L | 0.8 | 0.31
NO3, mg/L | ND (<0.1) | ND (<0.1)
HCO3, mg/L | 269 | 237
TDS mg/L | 323 | 459
223Ra, pCi/L | NA | 0.62±0.2
224Ra, pCi/L | NA | 2.47±0.3
226Ra, pCi/L | 0.8±0.11 | 19.82±0.66
228Ra, pCi/L | <0.2 | 1.72±0.21
226Ra+228Ra | <1.0 | 21.54
Ra, pCi/L | NA | 24.6
224Ra/228Ra | NA | 1.44
228Ra/226Ra | <0.25 | 0.09
U, µg/L | 0.3 | 0.75
*Composite analyses |  | 

## Slide 18: Laguna area
  Three of four anoxic
  All have low U, low Ra
  Low 228Ra/226Ra ARs suggest enrichment of U relative to Th in aquifer sediments
  224Ra/226Ra ARs >1.0 suggest presence of irreversible/slowly reversible sinks for Ra
  Ra and Ba sulfate precipitation (supported by high SO4 concentrations), or
  Effective sorption/ion exchange (groundwater low in Ca, Mg)
Well: | Laguna #1 | Laguna #2 | Laguna #3 | Laguna #4
pH | 7.78 | 7.73 | 7.94 | 7.13
DO mg/L | 0.7 | 0.31 | 0.25 | 2.2
NO3, mg/L | 0 | 0 | 0 | 1.81
HCO3, mg/L | 476 | 317 | 451 | 463
TDS mg/L | 630 | 945 | 734 | 618
223Ra, pCi/L | 0.017±0.023 | 0.123±0.072 | 0.046±0.031 | 0.009±0.014
224Ra, pCi/L | 0.68±0.05 | 1.82±0.13 | 0.85±0.07 | 0.52±0.04
226Ra, pCi/L | 0.69±0.06 | 3.16±0.19 | 1.84±0.11 | 1.11±0.08
228Ra, pCi/L | 0.72±0.09 | 1.21±0.11 | 0.67±0.09 | 0.3±0.08
226Ra+228Ra, pCi/L | 1.41 | 4.37 | 2.51 | 1.41
Ra, pCi/L | 2.01 | 6.07 | 3.29 | 1.87
224Ra/228Ra | 0.82 | 1.3 | 1.1 | 1.5
228Ra/226Ra | 1.05 | 0.38 | 0.37 | 0.27
U, µg/L | 0.1 | 0.4 | 0.7 | 1.9

## Slide 19: General trends
19
Samples with isotopic data indicating U enrichment in aquifer sediments plot along the carbonate dissolution line, indicating that processes raising PCO2 (microbial?) occurred in the presence of carbonate minerals.
CaCO3(s) + CO2(g) +H2O = Ca2+ + 2HCO3–
If CO2-generating processes are microbial, they must have occurred in the vadose zone at Glorieta (waters remained oxic). Can uranium in Glorieta groundwaters be sourced to carbonate dissolution in the vadose zone?
Zuni

## Slide 20: Conclusions
  Data are presented from three contrasting sites in bedrock aquifers, representing both reducing and oxic conditions, elevated U and Ra, elevated Ra alone, and low U and Ra.
  At each site, trends in Ra isotope ratios were successfully used to provide insights into sources and mobility of U and Ra in groundwater and aquifer sediments
  This study used an innovative, low-cost method for 226Ra determination with an inexpensive radon-in-air detector (RAD-7™); the method could be used for low-cost long-term monitoring or pilot tests for radium treatment