## Slide 1
Stability Analysis of Discontinuous Rock Slopes for the LH Open Pit Limestone Mine in Korea
S.K. Chung, E.S. park, Y.B. Jung,
C. Park, B.J. Lee, C. Sunwoo,
H.W. Kim, S.S. Kang, J.S. Kang
28 October 2013
Session No. 106
T75. Landslide Inventories, Data Dissemination, & Risk Reduction

## Slide 2: Outline
1
Introduction
1
Geological/Geophysical investigation
2
Numerical analysis for slope stability
3
Conclusions
4

## Slide 3
Geology of Korea & location
LH limestone
open pit mine

## Slide 4
Aerial observation of LH site

## Slide 5
Rock types in the study area
Granite
Leucocratic granite gneiss
Mica schist & sandy schist
(Myobong formation)
Carbonate rich limestone
Worm-eaten limestone
(Hwajeol formation)
basic & acidic dyke

## Slide 6
Geology of LH Open Pit Mine
F1
Fault AB
N40W/75NE
Fault A1
N65E/80SE
Fault B0
N20E/70SE
Fault E2
N20E/70SE
Fault F1
N20E/70SE
Fault A4
N35W/70NE
granite/gneiss
Schist
Lower limestone
Hwajeol formation
Upper carbonate rich limestone
Dolomite

## Slide 7
Result of geophysical survey on faults
Notes: The results of geophysical surveys are displayed on the aerial photograph of project area. Five DC resistivity survey lines were designed across the five major faults to investigate exact locations and shapes of the faults found from geological ground survey and weak zones around. One surface wave method survey line was designed across the AB fault to estimate in-site elastic modulus of fault zone.
Low resistivity structures in the results of DC resistivity survey which are continued from surface to the underground can be considered fault structure underground. Those structures are exactly coincident with real location of faults AB and A1 which are exposed due to excavation. Faults A2-A4 can be located on the road to the mine office from the DC restivity survey results of Zones A2-A4. Especially eastern part of Zone A1 shows low resistivity to the depth of around 20m. Which is considered it’s from dikes, severe weathering and joints and it could be checked in-situ exploration and aerial photos.
Surface wave method provided shear wave velocity map around fault AB. Shallow subsurface to the depth of 5m shows low velocity due to blasting disturbance and weathering. Fault zone also show 1/3-1/2 low velocity compared with the sound rock zone.

## Slide 8
Granite
Myobong formation
Lower limestone
Middle dolomite
Upper carbonate rich limestone
Hwajeol formation
Fault & Dyke
3-D Geological modeling

## Slide 9
Rock type | Deformation Modulus (MPa) | Poisson’s ratio | Cohesion (MPa) | Friction angle (˚) | Tensile strength (MPa) | Density (kgf/m3)
Limestone | 28,000 | 0.22 | 3.70 | 43 | 0.9 | 2,700
Dolomite | 33,000 | 0.22 | 4.30 | 44 | 2.4 | 2,850
Granite | 28,000 | 0.21 | 4.40 | 47 | 0.4 | 2,630
Schist | 15,000 | 0.19 | 1.95 | 42 | 0.7 | 2,800
Hwajeol formation | 28,000 | 0.22 | 3.70 | 43 | 0.9 | 2,700
Fault | 9,000 | 0.22 | 1.20 | 30 | 0 | 2,700
Mechanical laboratory tests
- Uniaxial & tri-axial compressive
strength test
- Indirect tensile strength test, etc.
Rock mass classification
- RMR (rock mass rating)
- GSI (geological strength index)
Empirical equations & Hoek-Brown method for estimation of geotechnical properties
- (MPa), (MPa), , ····
- (GPa)
Estimation of geotechnical properties

## Slide 10
Location of 2-D section (zone A:4-4’, B:2-2’, C:5-5’ & D:6-6’, E:1-1’, F:5-5’, G:3-3’)
확률론적 사면 안정성 평가 결과 (Section A)
Analysis type: LEM(Limit Equilibrium Analysis) + SSR(Shear Strength Reduction Method)
Selected sections for 2-D analysis
1
1’
2
2’
3
3’
4
4’
5
5’
6
6’

## Slide 11
PoF = 0.00%
Reliability index = 23.48
SF = 7.52
SF = 7.73
SF = 7.67
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone A: 4-4’
Stable
2-D model boundary
Result of analysis for Zone A

## Slide 12
PoF = 0.00%
Reliability index = 21.19
SF = 6.62
SF = 5.79
SF = 5.35
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone B: 2-2’
Stable
광산영향평가경계
광산영향평가경계
Result of analysis for Zone B
2-D model boundary
Boundary
of mine

## Slide 13
PoF = 0.00%
Reliability index = 8.43
SF = 9.30
SF = 9.38
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone C: 5-5’
Stable
도로
도로
Result of analysis for Zone C

## Slide 14
PoF = 0.00%
Reliability index = 9.06
SF = 8.97
SF = 8.77
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone D: 6-6’
Stable
도로
도로
Result of analysis for Zone D

## Slide 15
PoF = 0.00%
Reliability index = 11.85
SF = 8.68
SF = 6.13
SF = 6.13
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone E: 1-1’
Stable
광산영향평가경계
Boundary
of mine
Boundary
of mine
Result of analysis for Zone E
Boundary
of mine

## Slide 16
PoF = 0.00%
Reliability index = 16.67
SF = 8.81
SF = 10.26
SF = 9.02
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone F: 5-5’
Stable
Boundary
of mine
Boundary
of mine
Boundary
of mine
Result of analysis for Zone F

## Slide 17
Boundary
of mine
PoF = 0.00%
Reliability index = 17.06
SF = 20.86
SF = 10.78
SF = 10.52
Criteria
SF > 1.5
PoF < 0.1%
Reliability index > 3
Zone G: 3-3’
Stable
Boundary
of mine
Boundary
of mine
Result of analysis for Zone G

## Slide 18
Zone | LEM (Slide) |  |  |  | SSR (Phase) | Criteria | Stability
 | SF_L | SF_R | PoF | Reliability index, β | SF |  | 
A | 7.52 | 7.73 | 0.000% | 23.48 | 7.67 | SF > 1.5, β > 3, PoF < 0.1% | Stable
B | 6.62 | 5.79 | 0.000% | 21.19 | 5.35 |  | Stable
C | - | 9.30 | 0.000% | 8.43 | 9.38 |  | Stable
D | - | 8.97 | 0.000% | 9.06 | 8.77 |  | Stable
E | 8.68 | 6.13 | 0.000% | 11.85 | 6.13 |  | Stable
F | 8.81 | 10.26 | 0.000% | 16.67 | 9.02 |  | Stable
G | 20.86 | 10.78 | 0.000% | 17.06 | 10.52 |  | Stable
Summary of stability analyses

## Slide 19
MIDAS GTS (FE analysis program) & Strength reduction technique → FoS
3D slope stability analysis

## Slide 20
Zone | Min. FoS | Criterion | Remark
A | 7.73 | FoS > 1.5 | Stable
Maximum shear strain
Displacement magnitude
Maximum shear strain in faults
Result of 3-D analysis for Zone A

## Slide 21
Zone | Min. FoS | Criterion | Remark
B | 7.43 | FoS > 1.5 | Stable
Maximum shear strain
Displacement magnitude
Maximum shear strain in faults
Result of 3-D analysis for Zone B

## Slide 22
Conclusions (1)
The slope stability conditions at the LH open pit mine are governed mainly by the very continuous joints and faults. As a result of unfavorable combinations of directions of major joints and faults, local stability problems may occur at several places on the slope walls.
A series of extensive geological surveys were carried out to investigate the geological features including joints and faults, by using the surface geological mapping and 3D laser scanning.
Based on the stereographic projection technique it has been found that the orientation of main joints was divided into four sets in the area. When these joints are oriented approximately parallel to the slope wall, and have a dip angle steeper than that of the slope, sliding tends to occur unless the necessary stabilizing measures are taken in time. So, stability problems due to wedge and plane failure can occur locally in the slope wall.

## Slide 23
Conclusions (2)
Two- and three-dimensional numerical analyses based on the strength reduction method were conducted to investigate failure mechanisms in more detail and to explore the general characteristics of slope failure. From the numerical results, the overall stability of slopes was estimated by the criteria of the minimum value of safety factors and probability of failure.
As the rock mass class of the slope is greatly affected by the quality of blasting, a controlled perimeter blasting is a prerequisite for the stability of slopes and also for ensuring safe working conditions at lower levels of the mine.
As an early detection and remedy for unstable conditions is very important for economy and safety of the open pit mining, various monitoring techniques can be suggested for detecting unstable conditions of rock slopes and taking the necessary stabilizing measures in time.

## Slide 24
Thank you for attention !