## Slide 1: Stream flow hydrograph separation using end member mixing analysis on streams throughout the USA
Tonia Hack
William Sanford
Department of Geosciences
Colorado State University

## Slide 2: Approach
Separate hydrograph using 2-component end member mixing
Estimate baseflow
Compare to analytical methods: fixed interval, sliding interval, local minimum
Apply to various US streams

## Slide 3: Hydrograph Separation
2-component hydrograph separation
Analytical methods use constant time base of direct runoff from event to event (Linsley et al., 1982)
N = 0.8A0.2
  N is time in days after peak discharge that all discharge is considered baseflow
  A is watershed area in km2
Analytical methods use 2N* moving time window
  Odd integer between 3-11 closest to 2N
e.g. A=112km2 N=0.8(1120.2)=2.06 2N=2(2.06)=4.12 2N*=5

## Slide 4: Analytical Methods (Pettyjohn and Henning, 1979; Sloto and Crouse, 1996)
Sliding Interval
Fixed Interval Local Minimum

## Slide 5: Conductivity Mass Balance (CMB) Method (Stewart et al., 2007)
BF is daily baseflow
Q is daily discharge
QC is daily conductance
ROC is runoff conductance
BFC is baseflow conductance
Method chosen due to availability of USGS discharge and specific conductance data

## Slide 6: Study Sites
Groundwater regions from Thomas (1952)
Stream & Location | USGS # | UTM Coordinates | Drainage Area (mi2)
Buck Creek Longs SC | 02110400 | 33°57'12", 78°43'12" | 49.4
Silver River L'Anse MI | 04043150 | 46°48'15", 88°19'01" | 64.7
Sagehen Creek Truckee CA | 10343500 | 39°25'54", 120°14'13" | 10.5

## Slide 7: Preliminary Results
Chart: Buck Creek Longs SC
Chart: Date

## Slide 8: Preliminary Results
Chart: Silver River L'Anse MI
Chart: Date

## Slide 9: Preliminary Results
Chart: Sagehen Creek near Truckee CA
Chart: Date

## Slide 10: Preliminary Results
Stream | CUMULATIVE BFCMB DEPTH (cm over area) | METHOD | 2N* | CUMULATIVE UNCALBRATED BF DEPTH (cm over area) | % DIFFER-ENCE BFCMB : BFmethod | CALI-BRATED 2N* | CUMULATIVE CALIBRATED BF DEPTH (cm over area) | % DIFFER-ENCE BFCMB : BFmethod
Buck Creek Longs SC | 21.51 | Sliding Interval | 5 | 20.85 | 3.12 | 5 | 20.85 | 3.12
Silver River L’Anse MI | 40.84 | Sliding Interval | 5 | 77.9 | -62.42 | 31 | 40.96 | -0.29
Sagehen Creek Truckee CA | 26.33 | Local Minimum | 3 | 57.85 | -74.89 | 33 | 22.35 | 16.35

## Slide 11: Summary
2 component CMB shown to estimate baseflow
Snowmelt signal affects analytical method baseflow
  CMB estimates lower cumulative baseflow compared to analytical methods
Next steps include:
  Calculation of baseflow during periods of non-snowmelt
  Calibrate analytical method baseflow to CMB baseflow

## Slide 12: Thank You!