## Slide 1: Estimating Groundwater Recharge Using the Oklahoma Mesonet
Sam Wallace
Undergraduate, OSU Dept. Environmental Science
Dr. Tyson Ochsner
Assistant Professor of Soil Physics, OSU Dept. Plant and Soil Sciences

## Slide 3
Source: Oklahoma Water Atlas, 1983

## Slide 4: Groundwater Monitoring
USGS monitoring wells/streamflow gauges
  Real-time monitoring wells
  Daily groundwater monitoring
  Real-time stream flow gauges
Water Table Fluctuation Method
Water Budget Method

## Slide 5
Notes: How does knowing what groundwater recharge was weeks or months ago help us here?

## Slide 6: Groundwater Recharge Evaluation through Soil Moisture
Established statewide monitoring network
Long history of monitoring (since 1994)
Soil moisture monitoring at 5, 25, and 60 cm

## Slide 7: Our Study
Five Mesonet stations: Acme, El Reno, Fittstown, Shawnee, Spencer
Chosen for availability of both soil moisture sensors and groundwater wells.

## Slide 8: Methods
Mesonet temperature reference values converted to matric potential
Soil hydraulic parameters calculated using ROSETTA
Source: Illston et al., 2008

## Slide 9: Methods
Volumetric Water Content
Effective Saturation
Hydraulic Conductivity
Buckingham-Darcy Equation
Where:
q= water flux- groundwater recharge
K(Se)= hydraulic conductivity
Se= water content
h= matric potential
z= depth
θ(h) = volumetric water content θr = residual water content θs =saturated water content α = fitting parameter n = a measure of the pore-size distribution
K0 = a fitting matching point at saturation
L = empirical parameter

## Slide 10: Results
Station | Precip. (P) | Drainage (D) | D/P | Aquifer | Prior R/P | Reference
 | mm | mm | % |  | % | 
Acme | 768 | 77 | 10 | Rush Springs | 10 | Tanaka and Davis (1963)
El Reno | 817 | 42 | 5.1 | N. Canadian | 4.7 | Daniel (1999)
Fittstown | 917 | 97 | 11 | Arbuckle-Simpson | 12-14 | Fairchild et al. (1990) Christenson et al. (2011)
Shawnee | 864 | 28 | 3.2 | Garber-Wellington | 5-10 | Wood and Burton (1968) Carr and Marcher (1977)
Spencer | 895 | 108 | 12 | Garber-Wellington | 5-10 | Wood and Burton (1968) Carr and Marcher (1977)
Mean | 852 | 70 | 8.3 |  | 8.5 | 
Table 1: Mean annual precipitation (P), drainage at 60 cm (D), and the ratio D/P for five Mesonet stations using data from 1999 through 2011. For comparison, prior estimates of the ratio of groundwater recharge (R) to P are also shown.

## Slide 11: Results
Chart: ACME Groundwater Recharge and Mean Daily Groundwater Well Levels for the 2005 Water Year
Chart: FITT Groundwater Recharge and Mean Daily Groundwater Well Levels for the 2007 Water Year

## Slide 12: Discussion
Limitations in this new method
  No upward water flow
  Time lag varies with site, weather
Promising results
  Comparable to historical averages
  Calculated drainage events correspond to observed water table rises
As always, further research needed
  Does this method work in the extremes of the state?
  Mechanics of time lag
Source: Wikimedia

## Slide 13: Acknowledgements
I would like to thank the following sponsors:
Oklahoma State University Freshman Research Scholars Program
Oklahoma State University Wentz Research Project
EPA Greater Research Opportunities for Undergraduates Fellowship