## Slide 1: Potential over-development and aquifer co-mingling in the Hensell “Middle Trinity” aquifer; A study with bi-partisan management support
Jim Tucker
Baylor University – Southern Trinity Groundwater Conservation District – Clearwater Underground Water Conservation District

## Slide 2: Presentation Overview Part 1
Population Growth, Groundwater Production, and Management
  Extent of aquifer and identification of study area
  Growth locations and high production areas
  Purpose and cooperation between groundwater conservation districts in Groundwater Management Area 8
Introduction to the Middle Trinity Aquifer
  Regional stratigraphy
  Depositional environment

## Slide 3: Presentation Overview Part 2
Desired Future Conditions and Declining Water Levels
  Defining Desired Future Conditions
Co-mingling Between the Upper and Middle Trinity Aquifers
  Water migration into the freshwater Middle Trinity Aquifer from the high TDS Upper Trinity Aquifer
  Migration pathways, natural or artificial
  Chemical analysis of Middle Trinity water in the study area
Preliminary Conclusions

## Slide 4: Study Area – McLennan and Bell County, TX

## Slide 5: Population Growth and Production Needs
Texas populations are expected to increase by 60% by 2030
In central Texas this population growth is concentrated along the I-35 corridor, which runs through the study area
The Middle Trinity Aquifer is primarily produced to meet domestic, municipal, and agricultural demands
http://tti.tamu.edu/

## Slide 6: Population Growth and Water Level Declines
Population growth along I-35 is increasing production
Water levels declines along the I-35 corridor are compounded by clusters of high capacity wells
Water level changes 2011-2014 – CUWCD.org

## Slide 7: Introduction to the Middle Trinity Aquifer
The Trinity aquifer, stretches from Southern Oklahoma to Central Texas
It is a major aquifer system with three aquifers:
  Upper Trinity
  Middle Trinity
  Lower Trinity
The Middle Trinity or Hensell Formation is a freshwater sandstone aquifer
CUWCD.org

## Slide 8: Middle Trinity Aquifer
Keister, 2014

## Slide 9: Depositional Environment
The Middle Trinity aquifer or Hensell Formation is a sandstone that was deposited during the Cretaceous period
It is a result of a series of transgressive and regressive near shore shifts part of the Western Interior Seaway

## Slide 10: Groundwater Conservation Districts (GCDs)
Groundwater Conservation Districts were formed to serve as a management entity to protect and regulate the groundwater
Bell County – Clearwater Underground Water Conservation District
McLennan County – Southern Trinity Underground Water Conservation District
Funding for hydrogeologic research

## Slide 11: Declining Water Levels
Groundwater Conservation Districts manage their district, but the entire area has a hydrologic connection
LBG Guyton

## Slide 12: Declining Water Levels
Change in water levels 2006-2010
Keister, 2014

## Slide 13: Desired Future Conditions (DFCs)
The Groundwater Conservation Districts set desired future conditions or DFCs for a 50 year period
These DFCs are based on historic water levels changes, current production rates, and Managed Available Groundwater (MAG)
Middle Trinity DFCs
  Bell County: 286 ft/50 years or 5.72 ft/yr
  McLennan County: 489 ft/50 years or 9.78 ft/yr

## Slide 14: DFCs and Declining Water Levels
The Middle Trinity is experiencing observed water level declines ranging from 2-10 feet annually.
STGCD.org
CUWCD.org
-1.67 feet/yr
-12.44 feet/yr
DFC = 5.72 ft/yr
DFC=9.78 ft/yr

## Slide 15: Co-Mingling and Water Quality Degradation
The Upper Trinity aquifer or the Upper Glen Rose Formation is a highly fractured limestone bearing brackish water
The Upper Glen Rose is a formation with seams of gypsum that dissolve into solution causing high levels of total dissolved solids in the water
Decreasing head levels in the Middle Trinity may be allowing brackish water from the Upper Trinity to migrate downward, degrading water quality

## Slide 16: Possible Migration Pathways for Co-mingling
The pathway of migration may be natural, artificial, or both
The fractured nature of the Glen Rose limestone may provide a natural conduit for migration
Alternately, poorly completed wells may allow migration along the outer well casing, or through the well column in wells screened in both the Middle Trinity and Upper Trinity aquifers

## Slide 17: Migration Pathways

## Slide 18: Water Chemistry and Co-mingling
Within the study area, 26 wells were randomly selected to be sampled
The analysis focused on TDS and the ionic concentrations of Na, K, Ca, Mg, Cl, HCO3, and SO4
In the ion analysis, SO4 was used as a indicator for potential co-mingling, as gypsum (CaSO4) dissociates into Ca + SO4

## Slide 19: Water Chemistry Analysis
Stiff diagrams were generated to show spatial variation of the wells sampled within the study area

## Slide 20: Water Chemistry Analysis

## Slide 21: Preliminary Conclusions
Increased drawdown is occurring across GCD boundaries in the Middle Trinity in southern Bell County:
  Recommendations for cooperation in future management strategies will be submitted to the GCD boards
The water quality of the Middle Trinity in Northern Bell County appears to be adversely effected by possible co-mingling:
  Natural migration: water movement through fractured limestone in the Upper Trinity
  Artificial migration: poorly completed wells allow migration along the well column

## Slide 22: Cooperation with GCDs
Single County GCDs have historically managed their county without cooperation or sharing ideas with neighboring GCDs
Since the aquifers flow across county lines it is important to have GCDs working with each other to set similar DFCs
Through this research, lines of communication have been enhanced between the GCDs of Bell and McLennan County, with the hope that future management strategies will be implemented across district lines

## Slide 23
Special thanks to:
The Southern Trinity Groundwater Conservation District
The Clearwater Underground Water Conservation District
My Advising Committee: Dr. Yelderman, Dr. James, and Dr. Tubbs
Scooter Radcliffe
Dirk Aaron