## Slide 1
THE MISQUAMICUT STATE BEACH REPLENISHMENT PROJECT: ONE YEAR LATER, MEASURED USING RTK-GPS, DGPS AND BEACH PROFILES
Bryan A. Oakley1 Janet Freedman2, Robert J. Hollis3,
Danni R. Goulet2 and Jon C. Boothroyd3,4
Department of Environmental Earth Science, Eastern Connecticut State University
2. RI Coastal Resources Management Council
3. Rhode Island Geological Survey
4. Research Professor Emeritus, Dept. of Geosciences, Univ. of Rhode Island
National meeting of the Geological Society of America
2 November 2015 – Paper 162-9

## Slide 2
Field and Modeling Approaches to Understanding the Response of Coupled Barrier-Backbarrier Systems to Coastal Change
RIDOT
MISQUAMICUT (WESTERLY), RI – Post Sandy

## Slide 3
Misquamicut State Beach
Hs (Sandy)
9.8 m
Hs (Irene)
4.1 m
Microtidal (0.8-1.2 m), Wave dominated coastline
Notes: Microtidal (0.8-1.2m) wave dominated

## Slide 5
Before replenishment (August, 2013)

## Slide 6
18 April 2014 – View: East
Before replenishment

## Slide 7
During replenishment
65,000 m3 of sediment added to the berm
$3.1 Million ($47 m-3)
Sourced entirely from upland (glacial stratified deposits)
$$$

## Slide 8
28 May 2014 – View: East
After replenishment

## Slide 9
18 April 2014 (Pre)
30 May 2014 (Post)
Mapping the position of LHTS using sub-meter handheld DGPS

## Slide 10
MSQ-SB-1
MSQ-SB-2
MSQ-SB (3)
MSQ-SB-4
MSQ-SB-5
Beach profiles using the Modified Emery method (Monthly; pre/post storm)

## Slide 11
Last day of Replenishment – 30 May 2014
Topographic mapping RTK-GPS (Quarterly)

## Slide 12
Topographic mapping RTK-GPS (Quarterly)

## Slide 13
April 2015 Interpolated Surface

## Slide 14
Side-scan sonar mapping of the shoreface (2015-2016)

## Slide 15
Results – RTK Topographic Surveys
Change in Berm Elevation: 30 May 2014 to 3 April 2015

## Slide 16
Elevation Change: May 2014 – September 2014
Elevation Change: May 2014 – April 2015
Berm Volume: -11,500 m3 (-18% of replenishment)
Berm Volume: -14,600 m3 (-23% of replenishment)

## Slide 17
Post-Replenishment : 204 m3 m-1
April 2014
162 m3 m-1
April, 2015
168 m3 m-1
MSQ-SB Plotted Profile
April 2014 – April 2015

## Slide 18
Mapped Extent of
Depositional Platform
2015
2008
SO WHERE DID THE SEDIMENT GO?
2008
292,000 m2
2015
289,000 m2
Mapped Extent of Depositional Platform: 2008 - 2015

## Slide 19
Transport by easterly swells (Summer ‘14)
Deposition of replenishment sand on flood tidal delta
  Transport west by southwesterly ‘sea breeze’
Alongshore transport

## Slide 20
Wave Height (Hs)
0 2 4 6 8
Why the differential erosion…
Modeled “1%” significant wave heights – Block Island Sound
Grilli et al., 2015

## Slide 21
Conclusions
~14,000 m3 have been eroded at MSQ-SB, representing 23% of the placed volume during the first 15 months of the project
Alongshore sediment transport has dominated this process
The importance of shoreface processes and local shoreline orientation should be considered when designing beach replenishment projects
With replenishment; ‘Go Big or Go Home’!

## Slide 22
End of presentation
Thanks to:
Josh Bartosiewicz, Tim Ciskowski, Mike Manzi, Amber McDonald Cody Murphy, Brandan Sumeersarnauth (Eastern Undergraduates)
Greg Baribault, Rhode Island Coastal Resources Management Council
Dave Prescott, Save the Bay
Alan Comello (and staff), RI Dept. of Environmental Management