## Slide 1: Fast and Affordable Depths to Bedrock Using Geophysics
Dave Hart and Carolyn Streiff
North Central Geological Society of America Meeting - 2015

## Slide 2: Depth to Bedrock
Basic data for lots of land use planning and decisions
  a search on depth and bedrock in WDNR’s code gave 650 hits
How to determine best geophysical method to apply (criteria)
  Fast (< 2 hours to collect data)
  Relatively inexpensive (< $15K)
  Doesn’t require too much training (technical person)
  Reliable results (within 20 % of actual depth)
  Detects depths of interest (0 – 50 feet depth)
  Non invasive (no holes or disturbing crops)
  Portable (1 to 2 persons can carry)
Electrical Resistivity Imaging (ERI)
Passive Seismic (Horizontal Vertical Spectral Ratio method)

## Slide 4: Electrical Resistivity
Often overburden conducts electricity better than bedrock.
  Need to be in general area where this is true. (note example locations)

## Slide 5: Electrical Resistivity Imaging
Analogous to groundwater flow
Current electrodes like injection and pumping wells
Voltage electrodes like piezometers
Variations in materials cause flow lines to warp that can be seen in the voltages.
Multiple sets of electrodes allow image or tomography of subsurface.

## Slide 6
We can move the connectors by hand to get the different electrode combinations to see the bedrock at depth…

## Slide 7: Or we can let the box with a built-in computer and switches do it
Current Electrodes: Send and receive an input current into the ground
Potential Electrodes: Measure the difference in the input current
Moving these electrodes provides resistivity measurements at different depths and distances along the survey line.
Box can do either dipole-dipole or Wenner electrode combinations
Electrodes
Box

## Slide 8: Data Analyzed Software automatically matches resistivities w/data
> 1000 ohm m
< 100 ohm m
Sharp transition form blue to red (low to high) indicates quick change in geology from sediment to bedrock.
Seen at around 5 meters depth (16 feet)
Depth to bedrock around 15 to 20 feet here.
160 m
0 m

## Slide 9: Some Examples from around Wisconsin
Rountree sediment – Southwest Wisconsin
Homeowner Sinkhole – Iowa County
Mink River Wetland – Door County
Till – Calumet County
Les Voigt Fish Hatchery - Bayfield County

## Slide 10: Depth to bedrock in Southwest Wisconsin
Rountree formation caps many of the dolomite hills.
Mostly clay with varying thickness
Completed a study of dolomite quarries and Rountree

## Slide 11: Bown Quarry

## Slide 12: Line 1 – Parallel to Ridge
Sharp contact
Depth varies from 6 to 12 feet (2 – 4 meters)
Can also variation in bedrock
NE
SW

## Slide 13: Line 2 – Perpendicular to Ridge
Rountree can sometimes follow fractures
By filling and/or altering dolomite and enlarging the fractures.

## Slide 14: Sinkhole Investigation
Spring 2014
Spring 2015

## Slide 15
Initial appearance
Spring 2014

## Slide 16
Opened up
Spring 2014
2-3 feet width
20 foot depth (laser distance)
40 foot length (laser distance)
Repaired
  backhoe compaction
  Native fill
  5 yards of concrete

## Slide 17
Second Sinkhole
Spring 2015
Near road ~20 feet from previous
Typical for Wisconsin
Repaired with similar technique

## Slide 18
378
374
370
10 20 30 40 50 60 70 80
Distance (m)
Elevation (m) Line 1 (North)
Red>1000 ohm m
Blue<250 ohm m
378
374
370
10 20 30 40 50 60 70 80
Distance (m)
Elevation (m) Line 2 (South)
Dolomite
Bedrock
Sediment

## Slide 19: HVSR Passive Seismic
Records ambient noise or vibrations from wind, vehicles, other low frequency sources
Records all Frequencies between 0.1 cycles/second to 20 cycles/second
Fast data collection (20 minutes)
Some expertise to recognize good/bad data.

## Slide 21
Vibration Data
8 seconds shown, Total is 20 minutes
N-S
E-W
Vertical
Peak Ratio –
2.91cycles/second
73 feet depth

## Slide 22: Some Examples from around Wisconsin
Wisconsin River Valley
Tunnel Channel – Central Wisconsin
Little Plover River Basin – Central Wisconsin
Les Voigt Fish Hatchery - Bayfield County

## Slide 23
717.75
733.70
713.78
710.76
686.78
735.8
722.5
717.1
712.3
685.7
Elevations shown here
Depths to bedrock are generally less than 100 ft.
Decent agreement between coring w/geoprobe and passive seismic
Wisconsin River
Valley
Using Minnesota’s
a and b constants, matching to sediments.
(Chandler and Lively, 2014)

## Slide 24: Tunnel Channels
Mickelson and Syverson, 1997

## Slide 25: Tunnel Channels

## Slide 26: Tunnel Channels
Depths to bedrock are around 100 ft.
Bedrock Elevation is plotted to eliminated topography.
See lower elevations in the tunnel channel
Pre-glacial drainage or eroded while glacier was present?

## Slide 27: Questions?