## Slide 1
RISKING UNCONVENTIONAL SHALE PLAYS: A DIFFERENT APPROACH
Stephen R. Schutter
March 20, 2015
steveschutter10@gmail.com
Notes: In this time of cratering oil prices, it may seem a little strange that we should be talking about exploration for more. But how and why we look at these shales is integral to the process, and has been largely overlooked. Thinking about the way we do this may improve the process, both in terms of geological understanding and economic success. (Background is Upper Cretaceous Tropic Shale in southern Utah.)

## Slide 2
RISKING UNCONVENTIONAL SHALE PLAYS: A DIFFERENT APPROACH
1. Introduction – Why we need unconventional exploration
2. Risk and its uses
3. Concepts for evaluating shales and depositional models
4. Selecting variables
5. Example
6. Modeling conclusions and procedures
7. Summary
Notes: Risking unconventional shale plays - outline

## Slide 3
TIGHT OIL PRODUCTION - PROJECTION
EIA projection
Notes: (animated) This is a projection by the Energy Information Agency of the production of the principal tight oil plays through 2040 (by some accounts, this is a very optimistic projection, as horizontal wells tend to have steep decline rates). The point is that many of these plays are at or near their peaks, and there are no significant new plays in the pipeline. We need to have effective and efficient methods for finding new plays, as well as improving our understanding of existing plays. (Graph reprinted in J. David Hughes, 2014, Drilling Deeper: A Reality Check on the U. S. Government forecasts for a Lasting Tight Oil and Shale Gas Boom: Post Carbon Institute (postcarbon.org))

## Slide 4
RISK
Probability that optimum conditions are present in a given area with an economically sufficient volume of recoverable hydrocarbons present.
  (Technically and economically feasible)
Probability that an economically significant hydrocarbon accumulation exists in a specific location or in a play fairway, considering the probabilities of all possible variables.
  (Probability of economic success, designed for comparison to other prospects and plays)
Notes: Determination of which shales to study and how it will be done is based on the concept of risk. In its simplest form, this can be expressed as the probability that optimum conditions are present in a given area with an economically sufficient volume of recoverable hydrocarbons present. However, in industry this has been modified to the probability that an economically significant hydrocarbon accumulation exists in a specific location or in a play fairway, considering the probabilities of all possible variables. The first considers the possibility of success in a stand-alone framework; the second is intended for comparison among opportunities. The approach here will be the first, which can be used to guide decision-making in the process. It follows the location of the basin and stratigraphic interval of focus. (Background shale is the Cambrian Conesauga Shale at Helena, Alabama.)

## Slide 5
Standard/traditional methods assign values to a checklist of parameters, with each assigned a probability of success.
STANDARD RISKING
Since conventional plays include migration, assessment asks only if the parameters (threshold conditions) are met somewhere in the catchment areas.
Source
Reservoir
Seal
Maturation
Migration
Trap
Notes: The standard method of risking (the Rose method) works from a checklist of estimated values. Each needs to have a value assigned, and the results are multiplied, to give a value (probability of success) for the prospect or play. Note that because each factor is given equal weight, there is a tendency to think each is equally important, and not to discriminate between the relative value of different techniques. Conventional plays include migration, so assessment asks only if the parameters (threshold conditions) are met somewhere in the catchment areas. Because this risking procedure is generally used to compare prospects and plays, it is applied when the geological work is mature, and not used to guide decision-making during the process.

## Slide 6
The risking process can be incorporated into the exploration/evaluation process to help:
1. Identify the most important variables.
2. Focus efforts on resolving those variables.
3. Identify the area and stratigraphic interval where those variables are optimally combined (the “sweet spot”).
It should be based on an integrated study across a wide range of properties and characteristics, to minimize surprises and guard against unwarranted preconceptions.
Notes: The risking process can be incorporated into the exploration/evaluation process to help identify the most important variables, focus efforts on resolving those variables, and identify the sweet spots. It should be based on an integrated study of as many variables as possible, to minimize surprises and guard against unwarranted preconceptions. (Background photo is the Gothic Shale, near the Goosenecks. From the Ute Mountain Ute Tribe Gothic/Hovenweep farmout brochure, 2013.)

## Slide 7
TYPES OF SHALE RISK
Geological
What is the confidence level in the geological model?
What are the vertical and horizontal continuities of the relevant units?
Data
How representative are the data points of the larger system?
Does variation between data points support the exploration model?
Engineering
Can the shale resource be economically developed?
Does successful development depend on the orientation (azimuth) and distribution of geologic properties?
All types of risk can be reduced. Shale risk assessments can be dynamic.
Notes: (animated) Perhaps we need to think about unconventional shale plays differently. First, we should consider the factors that go into determining whether a shale can be adequately evaluated, and why. First, we need to think about geological risk. This would include (but not be confined to) assessment of the confidence level in the geological model. You also need to consider the vertical and horizontal confidence limits of the geological model. The data control also represents a risk: how much can you rely on the available data to represent the actual system? Engineering considerations also enter into consideration: can the shale resource be economically developed? Does the direction and distribution of development influence geologic properties (an example being the jointed Utica shale in the background)? Note that all types of risk can be reduced: by more data, better models, and new technology. Thus, assessments are dynamic, and answers can change. [Background is Utica black shale and siltstone with prominent joints, near Fort Palin, New York. Photo by Michael C. Rygel, 2008 (Wikipedia)]

## Slide 8
BLACK SHALES ARE NOT ALIKE
Source
Reservoir
Source
BAKKEN
Higher porosity lowstand siltstone, dolomite between highstand black shales
Source
Brittle
Reservoir
EAGLE FORD
Black shale source interval overlaps brittle reservoir
(transgressive/highstand)
Notes: When considering how to assess and risk black (organic-rich) shales it is necessary to realize that they are not all alike; there is no simple formula for predicting success in all of them. You need to determine how the shales are put together, and how success is achieved. For example, the Bakken has a lowstand reservoir sandwiched between two highstand source black shales. In contrast, in the Eagle Ford, the brittle reservoir rock overlaps with the source interval in the highstand.

## Slide 9
PARADOX AND MODELING
Probability of Storm Impact/Burial Event
Water Depth
Shallow/
High
Deep/
Low
In black shales, sedimentology, taphonomy, and OMT preservation demand rapid burial; stratigraphy indicates low average deposition. The answer to the paradox is episodicity, which is dependent on water depth.
If OMT, reservoir quality, and lateral continuity are dependent on water depth, they are statistically predictable, thus fulfilling the criteria for risk/assessment modeling.
Notes: (animated) One of the principal problems that has emerged in understanding black shales and their properties has been in how they are deposited. Arguments based on sedimentology, taphonomy, and organic matter preservation demand rapid burial; however, stratigraphic considerations (including biostratigraphic control) have indicated very slow rates of deposition. The answer to this apparent paradox is that deposition takes place in infrequent events, with long periods of non-deposition (or at least non-record) in between. Recognition of this permits the application of statistics to the questions of organic matter type, reservoir quality, and lateral continuity, which are dependent on how frequently events (most likely storm events) impact the bottom.

## Slide 10
Super- producing Interval
Total Productive
Interval?
SWEET SPOT EXPLORATION
Unconventional plays are concerned with finding the best possible combination of parameters (“sweet spots”).
Exploration and risking must be based on the areal distribution of independent variables..
Economic success depends on not simply reaching minimum conditions somewhere, but on the distribution and quality of “superproducing zones”.
Low TOC
Low TOC
2% TOC
12% TOC
γ Ray
Notes: Another consideration in assessing and risking shale plays is the location of “sweet spots.” Unconventional plays are concerned with finding the best possible combination of parameters (“sweet spots”). In the existing plays, this has been done by drilling a lot of holes; predictive geological models were not involved. Exploration and risking must be based on the areal distribution of independent variables. Economic success depends on not simply reaching minimum conditions somewhere, but on the distribution and quality of “superproducing zones.” (These would be comparable to the “superproducing zones” in carbonate reservoirs.) In the areas where parameters are most favorable, productive capacity is geometrically enhanced, resulting in “sweet spots.”

## Slide 11
MIDDLE ORDOVICIAN OIL SHALE AND K-BENTONITE
Notes: Oil shale and Deicke (aka Carimona) K-bentonite, Middle Ordovician Platteville Limestone, Faribault, MN. The oil shale is very thin, but sufficiently organic-rich to produce an oily film when it is drilled for local water wells and chips will reportedly burn. It is a common source rock, not only in the Upper Mississippi Valley, but also in the in the Simpson Group of Oklahoma and Texas (it looks very much like the Bromide). Similar shales are widespread across eastern North America, Scandinavia and Australia. The prize goes to whoever figures out how to exploit them first, and/or can determine which way the sweet spot is.
11

## Slide 12
RATE OF SEDIMENTATION AFFECTS OMT (ORGANIC MATTER TYPE)
0
HIGH
TOC
% TOC
0
HIGH
HUMIC
% HUMIC
0
HIGH
RoS
RATE of SEDIMENT
0
HIGH
CONODONTS
CONODONTS/KG
0
HIGH
% GONDOLELLA
Notes: (animated) Changes in rate of sedimentation (such as those produced regularly by eustatic sea level change) can impact the relative preservation of organic matter types. Historically, most analyses of black shales have relied on one value for organic matter type, and have not considered that the ratios may change systematically. At the most basic level, humic, land-derived material is more resistant to oxidation and alteration than is marine organic material. Thus, slower deposition during the transgression (rising sea level) not only favors higher levels of organic material (with decreasing sedimentary dilution), but also favors humic organic matter. In the theoretical example shown, sedimentation drops off, and the lower part of the shale contains strongly humic organic matter. As sedimentation begins to increase, less land-derived organic material is present, but the less stable marine organic material is also preserved. The abundance of conodonts is an inverse proxy for the rate of sedimentation; the percent of the conodonts that are Gondolella is a proxy for water depth. (Note that water depth and rate of sedimentation do not necessarily completely track each other, as sedimentation may begin to increase as the rate of sea level is declining, but not the absolute depth.)

## Slide 13
0
20
% TOC
40
0
500
CONODONTS/KG
0
50
% GONDOLELLA
M FT
0
0
1
2
3
1
STONER
EUDORA
CAPTAIN CREEK
% TOC
0
40
80
% HUMIC
% HUMIC
STANTON CYCLOTHEM
WINTERSET, IOWA
Notes: (animated) An actual example: relationship of organics and conodonts to the Stanton cyclothem near Winterset, Madison County, Iowa. Note that the highest levels of humic material are at the base of the black shale (as opposed to the highest percentage). Conodont abundance (a proxy for rate of deposition) also peaks there, although the percentage of Gondolella (a proxy for “offshoreness”) does not. The point is that your assessment of the quality of the black shale can depend on where you sample it, and can profoundly affect your evaluation. From Schutter, 1998, Figure 8.
13

## Slide 14
FACTOR ANALYSIS
Production
Factor
Factor A explains 75% of variation in production
Factor B explains 10% of variation in production
Exploration should focus on the most significant factors, and/or those most readily determined.
Factors (variables) can be dependent; linked or proxies for other factors.
Notes: (animated) In addition to having a geological model for how properties may be distributed within a shale, it is probably also advisable to focus on those properties which are most pertinent to success. Exploration should focus on the most significant factors, and/or those that are most readily determined. You don’t want to spend all of your effort or money on something that adds only incrementally to success. (This is an issue, if all factors are weighted equally in your risk assessment.) One approach may be factor analysis. More broadly, this may be considered variable analysis, although it may eventually involve stricter mathematical factor analysis (aimed at reducing the number of mathematical variables) or principal component analysis. For example, Factor A may explain 75% of the variation in production (a strong correlation). Factor B may explain only 10% of the variation. Clearly, it is more important to determine how to predict Factor A than Factor B. The factors can be weighted; if they have little or no value in determining either hydrocarbon prospectivity or contributing to the model, they can be given a lower priority or discarded. Risk calculations should be based on the significance of the factors. Understanding this can help you to direct your efforts to where they are most effective (including cost-effective).

## Slide 15
RISK BASIN
Thrust Belt
Foredeep
Shelf
Axial River System
Notes: Let’s consider an example of how this might work. We’ve identified a simple basin, a foredeep in front of a thrust belt, with an axial river prograding down the foredeep. We’ve also determined that our level of interest will be in an organic-rich black shale interval, where we are most likely to find an economic unconventional resource.

## Slide 16
90%
50%
10%
20 m
10 m
5 m
Thickness of superproducing zone
Continuity probability – Probability of continuity over 10 km
Low
Intermediate
High
Dilution by terrestrial organics
DISTRIBUTION OF MARINE ORGANICS
40% of variation above threshold
Notes: (animated) Consider the distribution of marine organics (the oil-prone organics) within the system. These would generally be expected to increase offshore, and be less diluted and more likely to be preserved. For the sake of the example, let’s consider that the abundance of marine organics represents 40% of the variation in oil production from the shale, above the threshold occurrence (that value determined either from valid analogs or from wells already drilled in the play). Other considerations on its distribution would be thickness of the superproducing zone (which determines not only how prolific it is, but how effectively it can be exploited by horizontal drilling), and the lateral continuity (how likely it is to be present, a real problem with horizontal shale wells).

## Slide 17
Onset Ro~0.5
OIL WINDOW
GAS WINDOW
Ro~1.2
MATURATION
30% of variation above threshold
Notes: (animated) Next, we will consider the distribution of maturity. This will probably increase under the thick sedimentary pile of the delta (to the right). For the sake of the example, maturation represents 30% of the variation in production from the organic-rich shale.

## Slide 18
Silica is dominantly qtz silt
BIOGENIC SILICA
5% of variation above threshold
HIGH
LOW
Notes: (animated) For a third variable, the presence of biogenic silica (which impacts brittleness, and hence frackability) accounts for 5% of the variation in production from the organic-rich shale. Note that the presence of silica is not a simple issue, in the same manner of organic matter type. It makes a big difference in your reservoir rock whether the silica is mobile biogenic silica or immobile silt. Again, this is something you need to consider in building your depositional and exploration model.

## Slide 19
MARINE ORGANICS
+ MATURATION
+ BIOGENIC SILICA
OUTCROP
OUTCROP
DATA-BASED UNCERTAINTY
Reliability
Notes: (animated) Consider how we might put the geologic model together, and think about how it might be impacted by our data base. By superimposing the various variables, we can come up with the “sweetest” spot available. (Because the opaqueness was based on the percentage impact, the most intense color is the sweetest – the oil window in the basin). To render it more pertinent, the margins of the basin have been eroded off. Thus, the sources of data on the organic-rich shale are the outcrop belts and the various wells. The white shading represents model uncertainty away from data control; this would be a risk factor. Note that in the basin, where there is more lateral continuity in the organic-rich shale, the data can be projected farther from control than it can be in the more highly variable deltaic environment. The overall approach is to evaluate the data that actually impact success (as opposed to checking boxes), which also highlights areas of uncertainty where work is needed to improve the risk assessment. Exploration priorities can be directed toward those things that have the most impact for the effort invested.

## Slide 20
SUCCESSFUL RISK MODELING REQUIRES DEPOSITIONAL/DIAGENETIC MODELS
γ Ray
Superproducing Zone
Black shales are deposited in dynamic environments, so lateral and vertical predictability depend on understanding depositional and diagenetic models.
Deposition and preservation depend on events, so statistics may be the best approach to estimate frequency and distribution.
Effective probability mapping is part of the process.
Probability is also important for below-resolution units:
- Superproducing zones are often thinner.
- Advances in technology may open new opportunities.
Care must be taken in comparing or generalizing about depositional environments.
Notes: (animated) Conclusion of principles slide: successful risk modeling requires depositional/diagenetic models. Black shales are deposited in dynamic environments, so lateral and vertical predictability depend on understanding depositional and diagenetic models. Deposition and preservation depend on events, so statistics may be the best approach to estimate frequency and distribution. Effective probability mapping is part of the process. Probability is also important for below-resolution units, as superproducing units are usually thinner (below seismic resolution). Advances in technology may open new opportunities. Finally, care must be taken in comparing or generalizing about depositional environments; having the right analog is important.

## Slide 21
LATERAL CONTINUITY
- Persistence of a unit over a given distance; may have a preferred azimuth.
- Should be statistically quantifiable; could be statistically incorporated into risk model.
- Probability should be mappable; reflects depositional patterns.
- Clearly an important variable in unconventional shales.
- Rarely generated, in spite of its significance in risk probability.
Notes: (animated) Lateral continuity is not a principal issue in the risking of unconventional shales, but does figure into how they should be evaluated. [Background picture is Manning Canyon Shale (Mississippian), western Provo Canyon, north-central Utah. From Schamel, 2008.]

## Slide 22
PROCEDURE
Identify analogs
- Which should have similar critical variables
Test depositional and diagenetic models against observations
- Improving success comes from better models
- Risk analysis needs to be based on effective models
Begin with broad evaluation of potential variables
- Objective is to identify critical variables, which may not be the same in all plays
- Find useful variables for understanding variation, and that can be effectively detected
- Calibration of integrated data permits extrapolation to previous studies, areas of limited data
Identify key wells, outcrops
- Sources of most diverse, well-documented data
Map significant variables
- Variables should be weighted by relative significance
- Optimum area is that with the highest score/hydrocarbon potential
Notes: (animated) Procedure (how to do it) – Begin with a broad evaluation of potential variables (which may not be the same in all plays), looking for variables that explain the most for the least effort, and calibrate it to utilize existing data. Identify the key wells and outcrops. Identify pertinent analogs. Test the depositional and diagenetic models against observations. Map the significant variables, weighted by relative significance. The optimum area is that with the highest score.

## Slide 23
SAMPLING STRATEGY FOR ANALYSIS
Sampling should be designed to integrate as many methods as possible across all lithologies in the section of interest.
Sampling should be designed to leverage preexisting data and test previous models as well as support new models.
Best approach may be core/outcrop based:
- May not be practical for all wells.
- Links to log and geophysical data emphasized.
- Early identification of “type” wells to establish parameters and variability for the play, with extrapolation.
- Because estimates are statistically based, more is always better, but not always practical.
Sampling needs to be at the scale of the “reservoir interval” or less.
- Depends on impact of “superproducing zones.”
Often below resolution of cuttings, sometimes below resolution of standard well logs.
Consider thickness of zone that can be practically developed.
- Is that likely to change with advancing technology?
Notes: (animated) Sampling strategy for analysis. Sampling should be designed to integrate as many methods as possible across all lithologies in the section of interest. It should be designed to leverage preexisting data and test previous models as well as support new models. The best approach may be core/outcrop based (as opposed to log/geophysics-based). Sampling needs to be at the scale of the “reservoir interval” or less; this is often below the resolution of cuttings and sometimes standard logs. But it is also necessary to consider the thickness of the zone that can be practically developed(which may change with technology).

## Slide 24
SUMMARY
The risking process can be dynamically incorporated into the exploration and evaluation process.
It can be used to focus on the most important variables and guide exploration efforts.
The purpose is to focus on the area and stratigraphic interval with optimum characteristics (the “sweet spot”).
Having an appropriate depositional and diagenetic model is critical to the process.
It can be used in conjunction with other, traditional risking methods.
Notes: (animated) Summary. (Background is Boquillas Formation, equivalent to the Eagle Ford, near Del Rio, Texas.)