## Slide 1
Potential for Underground Facilities in Granites of the Southeastern U.S.
Geological Society of America
2017 Southeastern Section Meeting 30–31 March, 2017, Richmond, VA
C. W. Myers
Former Division Director, Earth and Environmental Sciences Division—Retired
Los Alamos National Laboratory, Los Alamos, N. M.

## Slide 2
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Summary and Conclusions

## Slide 3
North American
Air Defense
Command
Cheyenne Mtn, CO
Underground Facilities---Military Use Examples
Dimona
(Negev Nuclear
Research Center )
Former USSR Underground
Submarine Base
Underground Hanger

## Slide 4
Underground Facilities—Civil Use Examples
http://bableenstimeline.weebly.com/..... http://www.megaliths.org/waterm/watermark.php?image=http://www.megaliths.org/photos/1457340597.jpg&watermark=watermark1.png
Transportation: Tunnels
Shelter and Protection
Energy: Oil and Gas Storage
Energy: Hydropower Station
Recreation: Swimming Pool

## Slide 5
Advantages and Disadvantages
Protection/Security
--terrorist and enemy attack,
--theft, sabotage,
--earthquakes
--electromagnetic pulse
--opacity
--access control
Landscape Aesthetics
Containment (hazardous materials)
Benign Environment
--constant temperature and humidity
--reduced vibration
--severe weather isolation
Lower Life-Cycle Cost
--lower utility cost
--lower insurance cost
--lower “exterior” maintenance
Low Flood Risk
Siting is key, engineered measures might be needed
Capital Cost
Generally high relative to an equivalent above-ground structure
Generic Underground Risks
Psychological Aversion
Misperceptions are Common
High Quality Rock Mass:
Underground Facility
Shaft Entry ?
Tunnel Entry ?
Constraints
  Geology
  Geography

## Slide 6
Advantages and Disadvantages
Protection/Security
--terrorist and enemy attack,
--theft, sabotage,
--severe weather, earthquakes
--electromagnetic pulse
--opacity
--access control
Landscape Aesthetics
Containment (hazardous materials)
Benign Environment
--constant temperature and humidity
--reduced vibration
--severe weather isolation
Lower Life-Cycle Cost
--lower utility cost
--lower insurance cost
--lower “exterior” maintenance
Low Flood Risk
Siting is key, engineered measures might be needed
Generic Underground Risks
Psychological Aversion
Misperceptions are Common
Underground Facility
Shaft Entry ?
Tunnel Entry ?
Constraints
  Geology
  Geography
Common Misperceptions
Capital Cost
Generally high relative to an equivalent above-ground structure
Generic Underground Risks
Psychological Aversion
6
Minimize Underground Construction Cost to Minimize Capital Cost
High Quality Rock Mass:

## Slide 7
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Summary and Conclusions

## Slide 8
Ground Support Requirements
…..minimize ground support cost by using high-quality rock masses
Reduce Construction Cost: 1. Use Locations with High Quality Rock…
~Opening Span,
or Height (meters)
Rock Mass Quality
Figure from: AGH University of Science and Technology (home.agh.edu.pl/~cala/hoek/Chapter3.pdf)

## Slide 9
Reduce Construction Cost: 1. Use Locations with High Quality Rock…
$
$$$
$$$$$
20m

## Slide 10
--automated, computerized drilling jumbos,
--more durable drill steel,
--advanced rock support,
--improved explosives, improved ventilation
Tunnel Boring Machine
Vertical Shaft
Sinking Machine
Shaft Boring Machine
(S. Zare and A. Bruland, 2007)
36% cost reduction—
(Study of 60m2 road tunnels
In Norway)
Photo sources: Dirlling.kr and Herrenknecht.com
Drill-and-Blast
Reduce Construction Cost: 2. Use modern excavation technology

## Slide 11
Avli
Reduce Construction Cost: 3. Tunnel (horizontal) entry might be possible if topographic relief is sufficient.
Avoid shaft entry if possible. Shaft sinking cost are usually higher
than tunneling cost….all other things being equal.
x
x

## Slide 12
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Summary and Conclusions

## Slide 13
Figure 1 from I. A. Speer, H.Y. McSween, Jr., and A.E. Gates, 1994, “Generation, Segregation, Ascent, and Emplacement of Alleghanian Plutons in the Southern Appalachians,” Journal of Geology, vol. 102, p. 249-267.
1. Large Granite Rock Masses are Relatively Abundant….

## Slide 14
2. Variety of Landforms and Exposures…
Domes and Dome-Like
Low-Relief
Quarries (shallow subsurface exposures)

## Slide 15
Favorable Geotechnical Properties
  Compressive strength:*
  Granite: 130,000kPa (19,000psi)
  Concrete: 43,000kPa (5,000psi)
2. Favorable Rock Mass Properties
    Potential for good to excellent geohydrological properties: massive, low permeability rock masses are known to exist.
Dimension-stone quarries in the southeastern U.S. provide direct evidence of the presence of large, granite rock masses, some with favorable geotechnical and geohydrological properties.
___________
*Intact rock values from www.engineeringtoolbox.com
Favorable Geotechnical Properties as Revealed
by Dimension Stone Quarries
  3. Large, Stable, Dry Underground Caverns
  Large-span (>15m)
  Largely self-supporting
  Relatively low unit-cost per cubic meter of underground space

## Slide 16
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Issues, Summary, and Conclusions
To be described in a presentation by Carpenter and others at this meeting

## Slide 17
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Summary and Conclusions

## Slide 18
Underground Business Complex:
SubTropolis, Kansas City, MO*
Fed Ex and UPS
Source: http://huntmidwest.com/industrial-space-for-lease/ and URL links.
World’s Largest Underground Business Complex – Former Underground Limestone Mine.
Tenant benefits
  6,000,000 square feet of industrial space
  Low lease rates---30% to 50% less than above-ground facilities
  Low utility costs---50% to 70% savings in total energy costs
  Constant temperature and humidity levels
  On-site services---management, maintenance, and 24/7 security.
Upfitting Ford Transit and F-150 Vehicles

## Slide 19
Archive Storage
SubTropolis (Continued)
Food and Commodity Storage
Data Center

## Slide 20
Underground Specialized Manufacturing Facility:
Brunson Instrument Company, Kansas City, MO
(high-precision, large-scale measurements)
Depth Below Surface | 77 feet
Ceiling Height | 12-13 feet
Factory and Office | 220,000 sq. ft
Examples of Brunson Instruments

## Slide 21
Quotes from Brunson Instrument Co. History* are Instructive
“N. Brunson formed the company in 1927 … business grew [but] vibrations from local street traffic and fluctuations in temperature became an increasing problem for the precise machining and adjustment processes…
…Mr. Brunson discovered that local geological
formations were nearly perfect for mining out
a vibration-free, temperature-stable space for
Manufacturing
….[Beginning in 1960] took 5 years to do the blasting and excavation needed to create this 220,000-square-foot underground facility…ideal setting for the production of high-precision instruments…
“The company has thrived in this environment ever since…. “
____________
*http://www.brunson.us/metrology-optical-measurement-products-alignment-about-brunson/metrology-optical-measurement-products-alignment-brunson-history/ 12/08/2016

## Slide 22
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Aboveground Cold Storage Facility
Issues, Summary, and Conclusions

## Slide 23
Example 3: Underground Data Centers (ultra-secure data centers are growing in number)
“…it resides in a former nuclear bunker about 100 ft. (30 m) below ground, sheltered behind 15.7 in. (40 cm) thick metal doors…”
Bahnhof’s Data Center in Stockholm

## Slide 24
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S.
Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Above-Ground Cold Storage Facility
Issues, Summary, and Conclusions

## Slide 25
Outline
Background on Underground Facilities
Advantages and Disadvantages
Reducing the Capital Cost of Underground Construction
Why Granite?
Examples of Possible Underground Facilities in Granites of the Southeastern U.S. Refrigerated Natural Gas Storage
Specialized Manufacturing/Commercial
Underground Data Center
  Regional FEMA and DHS Equipment and Supply Depots
Preliminary Analysis of an Underground versus Above-Ground Cold Storage Facility
Summary and Conclusions

## Slide 26
Work in Progress….
Above-Ground Cold Storage Facility
In the US, 88% used for food storage
Demand > Supply
Capital Cost
--$150 – $175/sq ft---cold storage w/house
--$50 - $60/sq ft ---conventional w/house
Ceiling Height
--22 ft. --20 years ago
--36 – 40 ft. --currently
Operating Cost
--25% is power cost for cooling
-------------------------------------------------------------------------------------------------------------------
Preliminary Result: Over time, the operations savings in lower cost for power, maintenance, etc. could possibly offset (partially? entirely?) the increased capital cost associated with underground construction.
Cold Storage Facility = Specialized Warehouse
Overview*
*“Perspectives on Cold Storage Investment Opportunities,” 2014, JLL, available at ww.cold-storage-investment-perspectives-jll-nov2014.pdf

## Slide 27
Underground facilities for specialized energy, commercial, and regional/national security applications can possibly be constructed in granites of the southeastern U.S.
---Capital cost: almost certainly higher
---Life cycle cost: almost certainly lower
Specialized needs examples:
  High levels of hardening, physical protection, and security
  Constant temperature and humidity
  Vibration-free environment
    Viability will depend critically on…
      Geology and hydrology
      Overall commercial viability
      Infrastructure availability and proximity
      Environmental risks, zoning restrictions, and public support
Local and regional economic benefits could be considerable
Summary and Conclusions

## Slide 28
Thank you for your attention
For additional information
myerswes@msn.com
Acknowledgements: ….highly useful discussions and input from:
  R. H. Carpenter
  J. C. Reid
  R. H. Cook
  W. H. McLemore