## Slide 1: Surficial Geology Map & Recharge Potential of the North Bennington Through Old Landfill Region David J DeSimone, PhD DeSimone Geoscience Investigations Petersburg, NY 12138 hawkeye272david@yahoo.com Vermont Geological Survey open file report VG2017-1 Vermont Agency of Natural Resources Contract #32310 submitted 26 December 2016

## Slide 2
Goals
> Complete 1:12,000 surficial geologic mapping of designated area largely within Bennington quad but edging into Hoosick Falls, Pownal and North Pownal quads.
> Interpret the Late Pleistocene through Holocene landscape evolution.
> Analyze ChemFab borings and work with Jon Kim, Emmet Norris & Peter Ryan to construct a fence diagram of that contaminated site.
> Use well logs to construct cross sections in the Old Landfill area & through any other places of interest.
> Generate aquifer recharge potential maps of the ChemFab & Old Landfill areas to aid in understanding downward movement of PFOA through overburden.

## Slide 3
Basic Map Elements
Flood plain = apple green
Alluvial fans = olive green
Fluvial terraces = mint green
Lake clay-silt = blue
Outwash = yellow
Ice contact sediments =
      shades of red-brown-pink
Till = grays
Bedrock = darkest gray
*See the map on poster*

## Slide 4: Landscape Elements & Pleistocene History   > Pre-glacial landscape with probable trellis-rectangular drainage network   > Walloomsac Valley cuts across lithologies/structures = antecedent   > Deep pre-glacial Furnace Brook valley at foot of Green Mountains with thick overburden   > Prominent ice contact sediments in Furnace Brook valley   > Hale Mountain ridge constrained retreating ice northwest of Old Landfill   > Shaftsbury ice margin records lowering of Lake Bascom & retreat from it left local lakes (Small & DeSimone, 1993; Libbey & Pierson, 1994)

## Slide 5: Paran Creek Detail     > Scoured valley walls, till with outcrop     > Remnant 700ft outwash     > Valley floor terraces & flood plain alluvium     > No residual lake clay-silt     Landscape Evolution     > Ice margin to north in Shaftsbury     > Lake Bascom drops from 900ft to lower levels including 700ft with outwash     > Drainage of Lake Bascom causes valley floor erosion     > Minor glacial lakes to the north drain and scour channel. (Lake Flat Top of Libbey & Pierson, 1994; Lake Emmons of Small & DeSimone, 1993)     Stratigraphy ? …

## Slide 6: ChemFab Fence Diagram   > Thin alluvium over bedrock in Paran Creek…Unit 3.

## Slide 7
Walloomsac Valley section also reveals 2 sandy terrace sequences that may correlate to Units 1 & 2 in the ChemFab fence diagram.
Draft

## Slide 8: Aquifer Recharge Potential   > Paran Creek alluvium does not inhibit downward flow of contaminants to bedrock aquifer.

## Slide 9: Old Landfill Detail   > Ice margin on NW side of ridge   > Stagnant ice to lee of ridge   > Typical landfill from half a century ago

## Slide 10: Two Cross Sections   > North & south of Old Landfill   > Thick sand & gravel   > Easy infiltration of PFOA into the subsurface   > Probable valuable overburden aquifer

## Slide 11: Conclusions   > Role of the surficial/Quaternary geologist in these investigations - geomorphology matters   * Interpret landscape evolution   * Interpret overburden stratigraphy   * 3-D distribution of sediments and their textures must fit the interpretation of landscape development   * Generate aquifer recharge maps for infiltration to either/both overburden and bedrock aquifers   * Identify possible pathways of waste migration   * Wind deposition of airborne contaminants & pattern of contaminated wells may be better understood if permeability of overburden is evaluated   > Synergy of having both surficial and bedrock expertise involved is invaluable   * We help each other…bounce ideas…even off the wall ones   * Modelers of bedrock aquifer flow must consider recharge through overburden