## Slide 1: GEOCHEMICAL ANALYSIS OF A SMALL URBAN FLOODPLAIN: FOURCHE CREEK BOTTOMS IN LITTLE ROCK, ARKANSAS
Jason Simmons1(jdsimmons1@ualr.edu), Laura S. Ruhl1, and Erik Pollock2
1Department of Earth Sciences, University of Arkansas at Little Rock
2Department of Geosciences, University of Arkansas at Fayetteville

## Slide 2
Fourche Creek Bottoms
Urbanization
Methods
Results and Discussion
Conclusions
References
Acknowledgements
Figure 1. Fourche Creek, Little Rock Arkansas
Roadmap

## Slide 3
Fourche Creek Bottoms
Drains 73% of the city before emptying into Arkansas River
Contains a natural wetland
Properties of the wetlands
  Wildlife Refuge
  Noise Absorbance
  Store 1 billion gallons of water
  Contamination filtration
Figure 2 and 3. Location map of Little Rock and Fourche Creek watershed (image retrieved from Google Earth and http://www.barbsnow.net/Arkansas.htm )

## Slide 4
Loss of pervious surfaces
Increased storm water runoff
Changes to hydrologic cycle
Changes in soil chemistry
Increased flooding
Figure 6. Water movement in urban vs natural landscapes (Lyons and Harmon, 2012).
The movement of water into a soil depends on land-surface slope, vegetation, degree of surface loading,and soil texture, structure, density and compaction. More watermoves into the soil zone on natural landscapes compared to urbanlandscapes with disturbed soils. These schematic drawings comparethe generalized disposition and movement of incoming water on anatural plant-covered landscape (A) with that in a disturbed urbanlandscape (B) with limited vegetation and abundant impervioussurfaces. MODIFIED FROM SCHEYER AND HIPPLE (2005)
Disruptions to natural landscape

## Slide 5
New sources of pollution
  Industrial
  Mining
  Sewage disposal and sewer overflow during flooding
  Metal contamination in car exhaust
  Greenhouse gas release
Watershed and water quality degradation
  Contaminants enters watershed via increased storm water runoff
Environmental Concerns

## Slide 6
Methods
Figure 8. Location map of sampling area (image retrieved from audubun.org; Google Earth)
Floodplains along Fourche Creek wetlands
3 transects chosen and GPS locations recorded
44 Surface (4-5 in.) samples collected at various distances into the floodplain
Transported to UALR and dried at room temp

## Slide 7
Methods
Grain size analysis performed
  Standard sieves and shaker
Leaching experiments performed
  10:1 liquid to solid ratio; deionized water
  Combine and react 24 hrs (+/-)2hr
  Centrifuged for 20 mins 10,000 rpm
  Filtered with .45um filter
Leachate analyzed
  Ion Chromatography (IC)
  Inductively Coupled Plasma Mass Spectrometry (ICP-MS)
Figure 10. Ion Chromatography, UALR lab
Figure 9. Standard Sieve, UALR

## Slide 8
Grain Size Distribution
Figure 12. Grain size at transect 1
Chart: Transect 1
| 0.0 | 3.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
>2mm | 0.65431 | 0 | 0.41841 | 0.10277 | 0 | 0.10163 | 2.2495 | 0.41026 | 0.30211 | 0.20387 | 0 | 0 | 0 | 1.7365 | 0.10204
1.00-2.00mm | 1.3086 | 2.8517 | 3.2427 | 0.8222 | 0.81218 | 1.1179 | 8.2822 | 1.2308 | 1.3092 | 1.9368 | 0.81466 | 5 | 0.5071 | 8.478 | 1.0204
.500-1.00mm | 21.265 | 32.1293 | 31.6946 | 25.4882 | 28.2234 | 28.8618 | 25.5624 | 31.6923 | 35.4481 | 30.8869 | 31.0591 | 35 | 28.8032 | 34.9336 | 33.1633
.250-.500mm | 29.4438 | 29.2776 | 28.1381 | 24.0493 | 24.3655 | 25.6098 | 23.8241 | 25.5385 | 24.2699 | 26.5036 | 26.7821 | 22.9592 | 25.2535 | 22.1655 | 27.9592
.125-.250mm | 19.084 | 17.8707 | 22.6987 | 16.7523 | 16.5482 | 15.8537 | 15.2352 | 16.2051 | 14.6022 | 17.5331 | 16.8024 | 16.6327 | 17.3428 | 12.9724 | 17.3469
.063-.125mm | 13.7405 | 11.4068 | 10.251 | 19.3217 | 15.9391 | 11.4837 | 10.2249 | 13.9487 | 11.6818 | 13.3537 | 13.1365 | 10.8163 | 12.6775 | 8.2737 | 11.2245
<.063mm | 14.5038 | 6.4639 | 3.5565 | 13.4635 | 14.1117 | 16.9715 | 14.6217 | 10.9744 | 12.3867 | 9.5821 | 11.4053 | 9.5918 | 15.4158 | 11.4402 | 9.1837
Chart: Transect 2
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0
>2mm | 0.30303 | 0.50659 | 1.524 | 1.2208 | 0.70779 | 0.20263 | 0.50201 | 0.31546 | 0 | 0.080483 | 0 | 0 | 0
1.00-2.00mm | 1.2121 | 1.2158 | 1.993 | 1.8311 | 1.1122 | 0.91185 | 0.50201 | 1.0515 | 0.40363 | 0.62374 | 0.20161 | 0.30832 | 0.40282
.500-1.00mm | 18.2828 | 14.387 | 22.3916 | 14.1404 | 20.5258 | 20.1621 | 24.2972 | 24.0799 | 32.3915 | 27.8672 | 26.2097 | 30.7297 | 35.6495
.250-.500mm | 22.1212 | 25.6332 | 23.6811 | 27.6704 | 26.5925 | 27.2543 | 26.7068 | 25.7624 | 24.8234 | 21.4286 | 25.9073 | 28.777 | 27.4924
.125-.250mm | 20.6061 | 21.8845 | 20.7503 | 26.4496 | 22.2447 | 21.3779 | 19.3775 | 16.4038 | 16.3471 | 15.996 | 20.2621 | 17.369 | 14.8036
.063-.125mm | 20.5051 | 17.2239 | 11.4889 | 12.1058 | 13.2457 | 17.1226 | 11.747 | 12.0925 | 15.1362 | 17.7062 | 20.0605 | 15.519 | 10.1712
<.063mm | 16.9697 | 19.1489 | 18.1712 | 16.5819 | 15.5713 | 12.9686 | 16.8675 | 20.2944 | 10.8981 | 16.2978 | 7.3589 | 7.297 | 11.4804
Figure 13. Grain Size at transect 2

## Slide 9
Figure 14. Grain size at transect 3
Chart: Transect 3
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0
>2.00mm | 0.91001 | 0 | 0.10081 | 0 | 0 | 0 | 0.40568 | 0 | 0.20141 | 1.3171 | 2.1277 | 0.20161 | 1.5015
1.00-2.00mm | 3.1345 | 1.005 | 0.70565 | 0.20305 | 0.40363 | 1.3185 | 2.4341 | 1.7137 | 3.8268 | 15.2989 | 5.0659 | 1.1089 | 5.4054
.500-1.00mm | 28.5137 | 27.5377 | 23.8911 | 20.4061 | 26.9425 | 30.2231 | 30.7302 | 35.2823 | 34.2397 | 38.6018 | 35.7649 | 32.8629 | 34.4344
.250-.500mm | 25.2781 | 23.0151 | 23.7903 | 23.8579 | 23.108 | 24.5436 | 22.5152 | 25 | 23.0614 | 21.2766 | 22.3911 | 24.496 | 22.5225
.125-.250mm | 18.8069 | 15.9799 | 16.0282 | 16.3452 | 15.2371 | 13.9959 | 14.6045 | 14.9194 | 13.6959 | 11.7528 | 14.1844 | 15.625 | 15.8158
.063-.125mm | 10.2123 | 17.5879 | 13.8105 | 12.4873 | 18.3653 | 10.142 | 10.142 | 10.2823 | 9.9698 | 6.2817 | 9.3212 | 10.8871 | 9.7097
<.063mm | 13.1446 | 14.8744 | 21.6734 | 26.7005 | 15.9435 | 19.7769 | 19.1684 | 12.8024 | 15.005 | 5.4711 | 11.1449 | 14.8185 | 10.6106
Overall fine to coarse grain sand
Transects 2 has largest amounts of fines
Slight variations in silt based on elevation changes in study area
  Transect 2 more flat floodplain
  Transect 1 and 3 steady elevation increase for first 10 feet
Homogenous grain size distribution at each location
  Due to size of the study area
  Quantity of each size present or washed away during a flood event
Grain Size Distribution

## Slide 10
Major Ions
IC measured concentrations of eight major ions
  Cations: calcium, ammonium, magnesium, sodium and potassium
  Anions: sulfate, nitrate, and chloride
Most of these constituents are highest at the water’s edge which could be due to greater interactions with and accumulation from the water
Figure 16. Fourche Creek Wetlands, metropolitan Little Rock

## Slide 11
Chart: Magnesium
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 2.6812 | 2.2749 | 2.4565 | 2.9429 | 2.0244 | 1.9087 | 2.5887 | 3.0092 | 3.9392 | 3.0313 | 2.7476 | 2.6316 | 4.2274 | 5.0793 | 4.6439 | 3.8505
Transect 2 | 4.9732 | 2.4245 | 3.2931 | 2.0784 | 1.6982 | 1.7391 | 2.5421 | 1.5062 | 1.5909 | 1.2003 | 1.8966
Transect 3 | 2.8703 | 1.3903 | 1.6493 | 1.5479 | 1.5588 | 1.1676 | 1.9656 | 0 | 1.577 | 2.4845 | 2.9303 | 2.5551
Chart: Calcium
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 15.7995 | 8.4379 | 10.7111 | 12.2403 | 7.3197 | 7.1238 | 8.7629 | 9.8902 | 12.5677 | 12.8405 | 9.7927 | 8.3645 | 10.5519 | 11.9241 | 11.8549 | 9.7541
Transect 2 | 28.5044 | 13.0407 | 17.4215 | 10.4467 | 8.6806 | 8.0763 | 11.6438 | 7.8671 | 6.5985 | 4.6897 | 6.4676
Transect 3 | 14.5213 | 5.5519 | 6.3843 | 5.5291 | 5.206 | 3.7579 | 5.3201 | 0 | 4.1517 | 7.0333 | 7.2293 | 5.8857 | 0
Chart: Ammonium
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 3.8179 | 4.2639 | 1.2999 | 0.853 | 1.826 | 2.7343 | 2.8059 | 3.761 | 1.7461 | 2.8193 | 3.2647 | 6.19 | 2.3677 | 3.2548 | 5.7598 | 4.8094
Transect 2 | 0.7276 | 0.2594 | 1.9555 | 1.1879 | 5.067 | 4.3325 | 4.2935 | 4.3306 | 2.6818 | 2.9632 | 5.7211
Transect 3 | 11.1347 | 1.2044 | 1.6816 | 1.0013 | 1.8808 | 0.8564 | 2.5149 | 0 | 0.971 | 2.0291 | 3.7658 | 1.6357 | 0
Figures 17-19. Cation concentration present in our floodplain
Ca+ and Mg2+ are naturally occurring
  Ca highest at water edge and decrease into the floodplain
  Mg decreases at transect 2, increases at 1 and 3
Ammonium (NH4+) enters via runoff
  Highest at creek bed of trans 3 then decrease. 1 and 2 increase into the floodplains
Cations
Notes: Previous Research reveals Ca and Mg removed from water in wetlands

## Slide 12
Chart: Sulfate
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 23.5791 | 15.4261 | 20.6669 | 21.5005 | 11.4346 | 0 | 6.0877 | 1.2215 | 0.8493 | 0.7091 | 1.1739 | 0.7956 | 0.4471 | 0.3954 | 0.8442 | 0.6049
Transect 2 | 41.8291 | 20.6147 | 28.0557 | 15.5262 | 7.8485 | 37.2398 | 4.0215 | 6.9088 | 3.9205 | 8.6949 | 4.3954 | 1.0583 | 1.1527
Transect 3 | 16.4932 | 9.4384 | 2.1642 | 0.9648 | 0.4377 | 0.4956 | 0.6381 | 0.241 | 0.2838 | 0.3806 | 0.2619 | 0.7292 | 0 | 0.5476 | 0.2859
Chart: Nitrate
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 2.9302 | 5.0604 | 2.0389 | 6.3789 | 1.7311 | 0 | 1.6347 | 3.2258 | 0.3479 | 0.652 | 0.561 | 0.9362 | 0.3906 | 0.3349 | 1.0385 | 1.2922
Transect 2 | 0.2533 | 0.2795 | 0.3649 | 0.4625 | 1.5896 | 2.7281 | 2.9005 | 4.3599 | 0.7466 | 1.2051 | 1.9209 | 1.3303 | 1.5862
Transect 3 | 13.6801 | 5.4993 | 2.9683 | 0.7457 | 0.3799 | 0.2711 | 0.4773 | 0 | 0 | 0 | 0.4874 | 0.8115 | 0 | 0 | 0
Chart: Chloride
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 0.8978 | 0.7635 | 0.4641 | 0.7512 | 0.7653 | 0 | 0.6757 | 0.4559 | 0.3716 | 0.1768 | 0.2033 | 0.2982 | 0.1612 | 0.1834 | 0.2609 | 0.2076
Transect 2 | 0.3892 | 0.338 | 0.3688 | 0.2486 | 0.208 | 0.6419 | 0.2173 | 0.2919 | 0.2128 | 0.202 | 0.1788 | 0.2029 | 0.2192
Transect 3 | 0.4302 | 3.864 | 0.2976 | 0.1731 | 0.1425 | 0.184 | 0.2917 | 0.1408 | 0.1116 | 0.1959 | 0.2237 | 0.3696 | 0 | 0.228 | 0.2963
Figures 20-22. Anion concentration present in our floodplain
All three are highest at the waters edge and decrease as you move into the floodplain
Anions

## Slide 13
ICP-MS measured concentrations of over 40 trace elements
All measurements varied with distance in the creek and location in the wetlands
Figure 23 and 24. Fourche Creek Bottoms

## Slide 14
Trace Elements
Chart: Manganese
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 0.27746 | 0.24477 | 0.53632 | 0.29887 | 0.071187 | 0.66102 | 0.56111 | 0.31799 | 0.4642 | 0.39076 | 0.4651 | 0.39957 | 0.43933 | 0.55342 | 0.72848 | 0.40636
Transect 2 | 5.7892 | 1.7988 | 1.7982 | 0.94371 | 0.54663 | 0.65376 | 0.68605 | 0.39766 | 0.42209 | 0.2335 | 0.13123 | 0.34681 | 0.46205
Transect 3 | 0.52579 | 0.1364 | 0.091285 | 0.12366 | 0.15057 | 0.070151 | 0.10333 | 0.080873 | 0.048977 | 0.33249 | 0.29478 | 0.094298
Figures 25 and 26. Selenium and Manganese concentrations
Se reached a max at 80 ft of trans 1
  Se can impact aquatic life
Mn decreases as you move into the floodplain
  Can adsorb other constituents and remove them from the water column
Chart: Selenium
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 0.20388 | 0.1836 | 0.13629 | 0.11601 | 0.37286 | 0.93389 | 2.7522 | 2.2114 | 2.9482 | 2.5832 | 1.8599 | 1.0894 | 2.8401 | 4.4624 | 2.9956 | 1.9411
Transect 2 | 0.12953 | 0.10925 | 0.095731 | 0.23768 | 0.55536 | 0.65675 | 0.70407 | 0.48101 | 0.38638 | 0.31203 | 0.25119 | 0.56212 | 0.69055
Transect 3 | 0.12277 | 0.38638 | 0.40666 | 0.81898 | 0.84602 | 0.25119 | 0.32555 | 0.50805 | 1.0556 | 1.2854 | 1.4071 | 0.4337

## Slide 15
Trace Elements
Chart: Lead
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 1.0041 | 1.9098 | 1.1551 | 2.0779 | 5.7142 | 12.5228 | 16.5713 | 10.1542 | 27.9306 | 9.8239 | 9.7236 | 5.6205 | 11.2541 | 10.4536 | 12.8764 | 11.1209
Transect 2 | 0.52927 | 0.4071 | 0.35245 | 0.92932 | 2.9711 | 3.5287 | 5.6841 | 2.7455 | 2.6422 | 1.6497 | 1.9125 | 3.9241 | 3.7228
Transect 3 | 0.71783 | 4.055 | 3.7049 | 5.5699 | 4.5788 | 0.7953 | 0.84967 | 1.4234 | 3.27 | 5.1667 | 5.6885 | 1.1766
Chart: Zinc
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 310.5699 | 178.4993 | 228.7534 | 252.7179 | 92.2608 | 157.559 | 252.8157 | 180.154 | 224.1929 | 192.2665 | 195.4784 | 101.4369 | 223.9285 | 243.8378 | 212.7709 | 190.7876
Transect 2 | 733.0805 | 273.7373 | 329.1354 | 133.0432 | 164.8662 | 138.1945 | 146.5228 | 90.1595 | 89.7578 | 90.7318 | 73.4745 | 87.8256 | 90.983
Transect 3 | 347.6914 | 51.4241 | 57.6876 | 84.4347 | 118.174 | 19.1448 | 20.879 | 23.6812 | 47.2603 | 110.4623 | 112.5153 | 18.7885
Figure 27 and 28. Zinc, and Lead concentrations
Zn decreases as you move into the floodplain
Pb increases from the creek into the floodplain
Both from anthropogenic sources (roadways)

## Slide 16
Trace Elements
Chart: Arsenic
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 0.43982 | 0.66126 | 0.52021 | 0.58228 | 1.7742 | 5.7053 | 13.6235 | 8.3223 | 10.851 | 8.5961 | 7.5741 | 4.3167 | 9.4461 | 11.1518 | 9.96 | 8.2079
Transect 2 | 0.6655 | 0.39327 | 0.40314 | 0.91234 | 2.6235 | 3.2612 | 4.3731 | 2.2708 | 2.3935 | 1.5908 | 1.5471 | 3.1681 | 3.6803
Transect 3 | 0.30582 | 1.5175 | 2.4359 | 3.5773 | 3.7426 | 0.93209 | 1.3426 | 1.6162 | 3.2655 | 4.4775 | 4.5721 | 1.2198
Chart: Cadmium
| 0.0 | 3.0 | 6.0 | 9.0 | 12.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Transect 1 | 1.5907 | 0.77656 | 1.1297 | 1.1933 | 0.20023 | 0.39912 | 0.14138 | 0.070964 | 0.066286 | 0.090947 | 0.10094 | 0.092533 | 0.081669 | 0.093088 | 0.087378 | 0.059863
Transect 2 | 6.6319 | 2.3288 | 2.7069 | 0.96892 | 0.96066 | 0.76584 | 0.73853 | 0.61594 | 0.3723 | 0.32366 | 0.27107 | 0.16827 | 0.16779
Transect 3 | 1.2342 | 0.14178 | 0.054312 | 0.04448 | 0.061449 | 0.029653 | 0.034886 | 0.019346 | 0.018156 | 0.057563 | 0.047414 | 0.015223
Figure 29 and 30. Arsenic and Cadmium concentrations
As reached a max at 20 ft of trans 1 and then increases
  Of concern for human health
Cd decreases into floodplain
  Associated with creek water

## Slide 17
We found consistent data linking the finest grain size to trace element concentrations within all locations
Several factors appear to affect the concentration in the sediment:
  Grain size
  Distance from the creek
  Amount of interaction with the creek water
  Nearby contaminant sources
Trace elements measured under USGS Geochemical Survey reference values for this area and EPA freshwater sediment quality guidelines
  Due to differences in testing; leaching vs acid dissolution
Conclusions

## Slide 18
Study Area
Industrial District
Mining Area
Figure 30. Study area and surrounding area (retrieved from Google Earth
Broader Impacts
  Locally affects fish and wildlife and humans who consume them
  Empties into Arkansas River
  This study helps provide a better understanding of urban wetlands role in ecological health
Conclusions Cont.

## Slide 19
Current work
To assess results as related to watershed health:
  Eleven surface samples collected in Feb 2018
  Two core samples
  Samples collected after a storm event
  In process of analyzing samples
  Background sample site chosen for comparison of all results

## Slide 20
References
Albanese, S. and Breward, N., 2011. Sources of anthropogenic contaminants in the urban environment. Chapter 8. In: Johnson, C.C.,
Demetriades, A., Locutura, J. and Ottesen, R.T., eds., Mapping the chemical environment of urban areas, Chichester, U.K., John Wiley & Sons, Ltd, 116-27.
Alvarez E, Perez A, Calvo R. 1993. Aluminum speciation in surface waters and soil solutions in areas of sulphide mineralization in Galicia (N.W. Spain). Sci Total Environ 133:17-37.
Agency for Toxic Substances and Disease Registry (ATSDR). Toxicological profile index. Atlanta, GA: U.S. Department of Health and Human Services, Public Health Service. https://www.atsdr.cdc.gov/ (accessed October 2017 – March 2018)
http://ar.audubon.org/fourche-creek (accessed October 15, 2017)
Chen, J., Theller, L., Gitau M. W., Engel, B.A. Harbor, J. M., 2016. Urbanization impacts on surface runoff of the contiguous United States: Journal of Environmental Management 187, p. 470-481.
De Vos, W. & Tarvainen, T. (Chief-editors) & Salminen, R. & Reeder, S. & De Vivo, B. et al. 2006: Geochemical Atlas of Europe. Part 2: Interpretation of Geochemical Maps, Additional Tables, Figures, Maps, and Related Publications. 690 p.
Eckel WP, Jacob TA. 1988. Ambient levels of 24 dissolved metals in U.S. surface and ground waters. Am Chem Soc Div Environ Chem 28:371-372.

## Slide 21
Elinder CG. 1985a. Cadmium: Uses, occurrence and intake. In: Friberg L, Elinder CG, Kjellström T, et al., eds. Cadmium and health: A toxicological and epidemiological appraisal. Vol. I. Exposure, dose, and metabolism. Effects and response. Boca Raton, FL: CRC Press, 23-64.
Elinder CG. 1992. Cadmium as an environmental hazard. IARC Sci Publ 118:123-132
Filipek LH, Nordstrom DK, Ficklin WH. 1987. Interaction of acid mine drainage with waters and sediments of West Squaw Creek in the West Shasta mining district, California. Environ Sci Technol 21:388-396.
Lyons, B.W. and Harmon, R.S., 2012. Why Urban Geochemistry: Elements, Vol. 8, p. 412-422.
Schueler, T.R., 1994. The importance of imperviousness. Watershed Protection Techniques vol.1 (30), p. 100-111.
Smith RA, Alexander RB, Wolman MG. 1987. Water-quality trends in the nation's rivers. Science 235:1607-1615.
United Nations, Population Division, Department of Economic and Social Affairs, 2017, World Urbanization Prospects, the 2017 Revision: Data Tables and Highlights; UN Directorate: New York.
U.S. Environmental Protection Agency. 1984a. Health assessment document for chromium. Research Triangle Park, NC: Environmental Assessment and Criteria Office, U.S. Environmental Protection Agency. EPA600883014F.

## Slide 22
U.S. Environmental Protection Agency. 1986a. Air quality criteria for lead. Research Triangle Park, NC: U.S. Environmental Protection Agency, Office of Research and Development, Office of Health and Environmental Assessment, Environmental Criteria and Assessment Office. EPA600883028F.
U.S. Environmental Protection Agency. 1986b. Quality criteria for water. Washington, DC: U.S. Environmental Protection Agency, Office of Water Planning and Standards. EPA440586001.
U.S. Environmental Protection Agency. 1995. National Primary Drinking Water Regulations: Barium {Technical Version}. https://nepis.epa.gov accessed December 29, 2017.
U.S. Environmental Protection Agency, 2003a. Health effects support document for manganese. U.S. Environmental Protection Agency. EPA822R03003.

## Slide 23
Acknowledgements
This study would not have been possible with out the help of Matt Carey who assisted in field sampling, and in providing much needed lab assistance. Funding for this project is provided by the UALR Signature Experience Grant.